## Slide 1: ME759 High Performance Computing for Applications in Engineering [Fall 2022]
Lecture Summary
Dan Negrut, 2022 ME759 UW-Madison

## Slide 2: The Hardware-Software Interplay [Big Segment]

## Slide 3: The ISA. The FDX cycle. Microarchicture aspects

## Slide 4: Computing requires instructions and data
An instruction: stored in memory as string of 0 & 1 bits (often 32 or 64 bits, you don’t have a say)
A piece of data: stored in memory as string of 0 & 1 bits (8 bits, or 16, or 64, etc. – can be even user defined)
In terms of storage and movement, there is no distinction between instructions and data
  Instructions are fetched & decoded & executed
  Data is used to produce results according to rules specified by the instructions
NOTE: the “data & instructions share same storage and pathways” paradigm formalized by von Neumann in late 1940s
  The “von Neumann model” (also known as the Princeton model)
Memory Data
Control Unit (CU)
Arithmetic Logic Unit (ALU)
data flow
instructions flow
internal consumption data
internal commands (uops)
Instructions
Data
[Cache] Memory
Processor
(Chip)
Notes: Also known as Princeton model
Harvard model (architecture): separate storage and pathways for data and instructions
This model relies on the FDX cycle
The process of processing instructions (FDX) intermediated by the processor’s CU

## Slide 5: The CPU’s Control Unit (CU)
The CU controls the “datapath” (i.e., the hardware collection of functional units + registers + data buses)
CU has several duties, such as
  Bringing in the next instruction from memory
  Decoding the instruction (possibly breaking it up into uops)
  Engaging in actions to enable “instruction level parallelism” (ILP)
CU manages/coordinates based on information encoded in the specific instruction it works on
Notes: The CU controls the DATAPATH (the functional units + registers + buses)

## Slide 6: The CPU’s Arithmetic Logic Unit (ALU)
Made up of a bunch of so called “execution units” or “functional units”
In charge of executing arithmetic and load/store operations
Examples:
  Arithmetic multiply/add unit (for integers)
  Arithmetic multiply/add unit (for floats)
  Special function unit
    Called upon to compute sin, cos, exp, log, etc.
  Etc.

## Slide 7: Instruction Set Architecture (ISA)
There is a limited number of prompts that the CU understands and thus act upon
This set of commands/prompts makes up the Instruction Set Architecture (ISA)
The same line of C code can lead to a different set of instructions on two different processors (CPUs)
This is so because two CPUs might implement two different ISAs
ISA: defines a “vocabulary” subsequently used by the compiler to specify the actions of a processor
Two more important schools of thought
  RISC: fixed set of bits coded by instructions (used to be 32, now it’s 64), simpler
  CISC: various lengths instructions (usually broken down to uops), more expressive, need more power to decode

## Slide 8: FDX Cycle
Each instruction goes through the Fetch-Decode-Execute (FDX) cycle
FDX is what keeps the CU and ALU busy
  FDX is done for instruction after instruction until program completes
Fetch: an instruction is fetched from memory
  Might look something like this (on 32 bits, MIPS, lw $t0, 12($s2)):
  10001110010010000000000000001100
Decode: this string of 1s and 0s are decoded by the CU
  Instruction type is baked into the operation code (opcode) for CU to refer to
Execute: once all data (operands) available, instruction is executed
  The execution can take several cycles of the CPU
Notes: Whatever ISA is used, at execution time these instructions need to be:
fetched (brought over from memory)
decoded (interpreted, to some extent “undoing” what the compiler did which was an encoding into ISA)
executed (dispatched to the ALUs)
All these are performed by the CU

## Slide 9: Decoding: Instruction Type I - immediate (MIPS ISA)
The first six bits encode the basic operation to be completed (opcode)
The next group of five bits: in which register the first operand is stored
The subsequent group of five bits: the target register, rt, where the result is written
The 16 bit stores the “immediate” value, usually used as the offset value in various instructions
  “Immediate” like in “immediate value”: no need to read other registers, we know all we need
op (6 bits)
rs (5 bits)
rt (5 bits)
constant or address (16 bits)
32 bits
Notes: For I instructions, the operation is completely defined by the opcode
addi $t,$s,C $t = $s + C (signed) 001000 sssss ttttt CCCC CCCC CCCC CCCC

## Slide 10: Decoding: Instruction Type R - register (MIPS ISA)
Type R has the same first three fields op, rs, rt like I-type (note: now, rt is the second source register)
Packs three additional fields:
  Five bit rd field (register destination)
  Five bit shamt field (shift amount, only used for “shift” instructions)
  Six bit funct field, which is a function code that further qualifies the opcode
op (6 bits)
rs (5 bits)
rt (5 bits)
rd (5 bits)
shamt (5 bits)
funct (6 bits)
32 bits
Notes: DAN: see http://courses.cs.washington.edu/courses/cse378/09au/lectures/cse378au09-04.pdf for a nice discussion of I and R type instructions

## Slide 11: Decoding: Instruction Type J - jump (MIPS ISA)
Type J has an op field and an address field
Jump instruction has a word address, not an offset
  A 26-bit address field allows for jumps to any address between 0 and 226-1
Longer jumps use the “jump register” instruction: jr $ra # jump to address in register $ra
op (6 bits)
address (26 bits)
32 bits
[http://www.divms.uiowa.edu/~ghosh/1-24-06.pdf]
Procedure called
first time here
Procedure called
second time here
Execution
instructions
Notes: For J instructions, the operation is completely defined by the opcode.
Just two J-type instructions (j and jal). These set the PC register!
Can jump to an address less than 256 MB
jr is R-type

## Slide 12: FDX Cycle – The Execution Part: It all boils down to transistors…
How does the FDX magic happen?
  Transistors are organized into complex logical units capable of performing simple operations
  With lots of transistors come opportunities for building/implementing in silicon additional functional/control units that can operate at the same time towards a shared goal
Transistors:
  Step 1: used to perform tasks (tied to CU and ALU use)
  Step 2: used to store data and instructions
Notes: A transistor (when used in a CPU) is essentially a switch, like a light switch except that you don't have to turn it on or off manually. Rather, it is controlled by an electrical current. The most important thing to understand is that modern computers are two-state devices: the only thing that really matters is whether a wire has a current or not.

## Slide 13: Transistors at work: AND, OR, NOT
Truth tables for bitwise AND, OR, and NOT
AND and OR logical ops require two transistors
The NOT logical operation is implemented using one transistor
AND | in2=0 | in2=1
in1=0 | 0 | 0
in1=1 | 0 | 1
OR | in2=0 | in2=1
in1=0 | 0 | 1
in1=1 | 1 | 1
NOT | 
in1=0 | 1
in1=1 | 0
AND
OR
NOT
Notes: Functional completeness: NAND + NOR
Also: AND + NOT

## Slide 14: Integrated Circuits-A One Bit Combo: OR, AND, 1 Bit Adder
1 Bit Adder, the Sum part
A One Bit Combo: OR, AND, 1 Bit Sum
  Controlled by the input “Operation”
result
Notes: Main idea: combine simpler blocks to get a more complex block
Throw in a multiplexor (a “selector”) and you can build a more complex “LEGO brick”, a COMBO

## Slide 15: Integrated Circuits: From Transistors to Chip Microarchitecture
Notes: Trend: simple to complex

## Slide 16: Registers

## Slide 17: Registers, quick facts
A register is a hardware asset whose role is that of information storing
  Information: data value or instruction
A register is the storage type with shortest latency – part of the CU & ALU combo
  Latency – can be of the order of hundreds of picoseconds
The size and number of registers are specific to an ISA
  To start off, the size of the register is 32 bits (used to be, now 64 bits)
  Number of registers: Back in the day, for the MIPS ISA, there were 32 registers (no more, no less)
Notes: Typically, an n-bit register might require 4n … 8n transistors
Note: MIPS64 also uses 32 registers
Don’t expect to see too many registers: precious commodities which are located on prime real-estate

## Slide 18: Register Types (1/2)
Current Instruction Register (CIR) – holds the instruction that is executed
  Sometimes known as “instruction register” IR
Program Counter (PC) – holds address of the instruction executed next
  NOTE: unlike CIR, PC contains *address* of the instruction, not actual instruction
  Sometimes called IAR: Instruction Address Register
Memory Data Register (MDR) – holds data read in from memory or, alternatively, produced by the ALU and waiting to be stored in memory
Memory Address Register (MAR) – holds address of RAM memory location where input/output data is supposed to be read in/written out
  NOTE: unlike MDR, MAR contains *address* of a mem location, not actual data
Return Address (RA) – the address where upon finishing a sequence of instructions, the execution should jump and commence with the execution of subsequent instruction
Notes: An utility that monitors the program counter can tell you what the hot spots of your executable are
PC is used by profilers to see which instructions are hot-spots

## Slide 19: Register Types (2/2)
There are several other registers common to many chip designs
  These are encountered in different numbers (also depending on ISA)
Since they come in larger numbers they don’t have an acronym
  Registers for Subroutine Arguments (4) – a0 through a3
  Registers for Temporary Variables (10) – t0 through t9
  Registers for Saved Temporary Variables (8) – s0 through s7
    Saved between function calls
Several other registers are involved in handling function calls
Summarized below, their meaning only apparent in conjunction with the organization of the virtual memory
  Stack Pointer (sp) – a register that holds an address that points to the top of the stack
  Global Pointer (gp) – register that holds on to a global pointer that points into the middle of a 64KB block of memory in the heap that holds constants and global variables (these objects can be quickly accessed with a single load or store instruction)
  Frame Pointer (fp) - a register that holds an address that points to the beginning of the procedure frame (for instance, the previous sp before this function changed its value)
Notes: Virtual memory – at the end of this segment

## Slide 20: Pipelining
  “Nothing is particularly hard if you divide it into small jobs.”
  --Henry Ford, founder of Ford Motor Company [1863 –1947]

## Slide 21: Clock Cycle: time before the assembly line move again
The processor
  “clock cycle”: the amount of time between two ticks of the internal clock of the microprocessor (chip)
  Microprocessor clock speed typically measured in Hertz (pulses per second): number of pulses per second
FDX “Generic” process -- these stages can represent any instruction (though not all needed):
  Stage 1: Fetch an instruction
  Stage 2: Decode the instruction
  Stage 3: Data access
  Stage 4: Execute the operation (e.g., might be a request to calculate an address)
  Stage 5: Write-back into register file
Tasks can be worked upon simultaneously when they are in different stages (at most 5)

## Slide 22
Rules of thumb: costs to eXecute an operation > 1 clock cycle [refers to older MIPS ISA; cost of X in FDX]
22
Eg. 4 clock cycles for SW, 5 clock cycles for LW, 4 clock cycles for add, etc.
Each stage takes a certain number of cycles
  A stage has substages
  This sequence of substages present the opportunity to pipeline
Notes: The numbers for the X86 family of chips is usually different

## Slide 23: Pipelining Benefits: faster execution & no code rewrite
Benefit 1: faster execution, owing to simultaneously working on multiple instructions
  Assume that you have
    A very large number of instructions
    Balanced stages
    A pipeline that is larger than or equal to the number “” of stages associated with the typical ISA instruction
  If 1 through 3 above hold, in a first order approximation, speed-up you get out of pipelining is approximately “”
Benefit 2: no code rewrite required on the user’s part; no effort needed to reap benefits
  This kind of parallel processing of stages is transparent to the user
  Unlike GPU or multicore parallel computing, you don’t have to do anything to benefit from it
Notes: Ideally: at each cycle you complete one instruction
This ignores the need to “prime” the pipeline and to pipeline shutdown.
This ignores hazards (see next)
NOTE: this is not parallel programing, but rather parallel execution (it’s out of the programmer’s hands)

## Slide 24: Pipelining, Good to Remember
Balanced pipeline: each of pipeline stage takes the same amount of time to complete
Non-balanced: will be stations that wait for the laggard station at every single cycle
Common sense: If there is a station that takes a significantly longer time since it does significantly more than other stations, it should be broken into two and the length of the pipeline increases by one station
  Leads to deeper pipelines
  Typical pipeline depth today: 12-15 stages
The amount of time required to complete one stage of the pipeline: one clock cycle
Pipelined processor: one instruction retired at each clock cycle
Non-pipelined processor: no overlap when executing instructions
Important Remark:
  Pipelining does not decrease the time to complete one instruction but rather it increases the throughput of the processor by overlapping different stages of processing of different instructions
Notes: NOTE: an individual instruction may take longer to complete (because some stages are delayed to fit the common tick)
The issue here is so-called INSTRUCTION HETEROGENEITY
Ford solved this problem by limiting the number of options:
“Any customer can have a car painted any color that he wants so long as it is black.”
But the benefit is THROUGHPUT

## Slide 25: Deep Pipelines Plagued by Pipelining Hazards
Structural hazards: the possibility of having a combination of instructions in the pipeline contending for the same hardware asset
Data hazards [very common]: value used in the instruction is unavailable
Control hazards: a corresponding machine instruction decides the program flow
[Patterson, 4th edition]→

## Slide 26: Pipeline Structural Hazards
Solution 1: perhaps a register can be commandeered somehow, for temporary use
  Fortuitous, a matter of serendipity
  Increase number of registers?
    Brute force solution; expensive and consequential (requires a chip design change, perhaps even ISA)
    Note that “needing one extra register” is just one possible scenarios; there are might be other contention scenarios lurking
Solution 2: serialize the access, basically introduce a bubble in the pipeline so that there is no contention
  “bubble in the pipeline” – think of it as a skipped issue slot (the scheduler can’t issue anything)
  Introducing bubbles into the pipeline at run time slows down the execution
Solution 3: Out of order execution (OOOE) done statically (at compile time) or dynamically (at run time)
  Good compromise
Notes: Analogy: we finished eating well before the dinner table is clean, the plates are in the dishwasher, and the floor is swept

## Slide 27: Pipeline Data Hazards (2/2)
Resolution [less than ideal]: Put bubbles in the pipeline to wait for the first instruction to fully complete
Alternative [the good] Resolution: use “forwarding” or “bypassing”
Key observation: the value that will eventually be placed in $t0 is available after stage 3 of the pipeline (where the ALU actually computes this value)
    Analogy: we finished eating well before the dinner table is clean, the plates are in the dishwasher, and the floor is swept
Provide the means for that value in the ALU to be made available to other stages of the pipeline right away
  Avoids bubbling - don’t have to wait several cycles before the value made its way into $t0
  This process is called “intermediate result forwarding”
Supporting forwarding does not guarantee resolution of all scenarios
  Occasionally the pipeline ends up with bubbles for a couple of cycles
OOOE helps (insert unrelated instruction, wedged between two instructions that depend on each other)
Pipeline Data Hazards
[very common]
Notes: Analogy: we finished eating well before the dinner table is clean, the plates are in the dishwasher, and the floor is swept

## Slide 28: Pipeline Control Hazards: Branch Prediction
Should we bubble the pipeline while this instruction is fully processed and branching decision becomes clear?
  If yes: strategy always works, but slows down execution
  If no: rely on branch prediction and proceed fast but cautiously
Static Branch Prediction :
  Several heuristics for proceeding: for instance, for a do-while construct it makes sense to always be jumping back at the beginning of the loop
    Similar heuristics can be produced in other scenarios (a “for” loop, for instance)
Dynamic Branch Prediction :
  At a branching point, the branch/no-branch decision can change during the life of a program based on recent history
  In some cases, branch prediction accuracy hits 90%
  Use with if-then-else statements
Note: when your prediction is wrong you have to discard the [micro]instruction[s] executed speculatively and take the correct execution path
Notes: Dynamic branch prediction: requires more hardware to implement the logic (keep track of previous paths)

## Slide 29: [New topic]Pipelining vs. Multiple-Issue
Multiple-issue: In sequential computing, a multiple-issue processor core has the hardware chops to issue more than one instruction per cycle
Pipelining different than “Multiple-Issue,” which is another way of speeding up execution
  Pipelining: the next step is dependent on the previous step
  Multiple-Issue: the steps next to each other are independent (see code snippet below)
On average, more than one instruction is processed by the same core in the same clock cycle
Multiple-Issue can be done statically or dynamically
  Static multiple-issue:
    Predefined, doesn’t change at run time
    Who uses it: Intel, in AVX512 (but not only)
  Dynamic multiple-issue:
    Determined at run time, the chip has dedicated hardware resources that can identify and execute additional work
    Who uses it: Intel, AMD, IBM, NVIDIA, etc.
int a, b;
float c, d;
//some code setting up a, b, c, d
a += b;
c += d;
Notes: Depart from the “assembly line” analogy. Here, think of a car manufacturing plant where more car models are produced simultaneously, by sharing common available resources (stations).
It’s actually good here to have very different “car models”: it’s less likely to have competition for same resources (stations).

## Slide 30: Pipelining vs. Multiple Issue
[Modern Operating System, Tanenbaum-Bos]→
(a) Three-stage pipeline
(b) Multiple issue processor

## Slide 31: Attributes of Dynamic Multiple-Issue
The data dependencies between instruction being processed takes place at run time
Checking for dependencies is complex, requires high cost in time and energy
Checks in place to make sure result is ok
  “ok”: no difference if the instructions are executed “multiple-issue” or “single issue”
NOTE: a chip that can do multiple-issue is also called a superscalar architecture
Notes: CU acts as supervisor to see what instructions can be issued and dispatched simultaneously

## Slide 32: Instruction-Level Parallelism (ILP) [belongs to a single specific thread of a process] & Thread Level Parallelism (TLP) [happens on a single core]
ILP:
  Including Pipelining, OOOE, and multiple-issue
  ILP is a property of a program
  ILP is an IPC (Instruction Per Cycle) that:
    Processor does the entire instruction in one cycle
    Processor can do any number of instructions in the same cycle
  Important: these instructions belong to the same program or process; i.e., belong to one thread
    “process” – how the operating systems calls your program
TLP:
  chip executes simultaneously instructions from different processes or different threads
  Important to keep in mind: we are talking about parallelism on one hardware core, not multicore
Difference:
  Recall concept of “Program Counter” (PC): a register that holds address of next instruction
  ILP == all instructions executed by the chip in parallel are associated with one PC
  TLP == the stream of instructions simultaneously processed by the chip associated with more than one PC
Notes: Dynamic multiple-issue makes use of a buffer for instructions to be able to look ahead.
We already alluded to other ILP techniques:
out of order execution
speculative execution and branch prediction
also, register renaming, etc.

## Slide 33: Process vs. thread – getting a bit into the weeds
There is a subtle difference between processes & threads:
  TLP is what happens when two processes such as Matlab and Microsoft Word run on the chip
    Because two different processes, there are two different PCs
  TLP: two (or even more) OpenMP or POSIX threads simultaneously run on the chip
    Because two different threads, there are two different PCs
How similar: Both processes and threads are independent sequences of execution
How different:
  Threads (of the same process) run in a shared memory space
    This is how shared-memory parallel computing takes place. Like OpenMP
  Processes run in separate memory spaces
    This is how distributed-memory parallel computing takes place. Like MPI*

## Slide 34: Each thread has its own register file, stack; but not memory space
[Mirela Damian]
Physically, it runs on one core
(one CU, one ALU, one register file)
Physically, it runs on one core
(one CU, one ALU, one register file)

## Slide 35: Multi-threading makes the full use of TLP
Multi-threading, a possible taxonomy (Hennessey & Paterson)
  Coarse grain multi-threading
    The Instruction Control issues instructions from one thread for many cycles
    Instruction Control switches to issuing from another thread only when the first thread runs into a long-latency operation
      Examples: cache miss, interrupt, etc.
      “long-latency”: Hundreds of cycles or so
  Fine grain multi-threading
    Instruction Control can issue instructions from a different thread each cycle
    “Barrel-gun style” processing: thread from where next instruction is picked for execution can change at every cycle
      Examples: GPU computing similar to this
    More nimble/sophisticated compared to coarse multi-threading
  Simultaneous multi-threading
    Instruction Control can issue instructions from different threads in the same cycle

## Slide 36: Superscalar processor or TLP processor
Superscalar vs. TLP
  Superscalar: instructions associated with one PC
  TLP: instructions associated with two PCs
Superscalar: one PC on the chip
  HW has the means to execute more than one instruction per cycle
  Superscalar: it’s more than a “scalar”; i.e., one thread
TLP: Processor handles instructions from different threads/processes
NOTE: we are not talking about multiple-cores; we are still talking about one CPU core here

## Slide 37: Measuring Speed of Execution

## Slide 38: Nomenclature
Wall Clock Time
  Amount of time from the beginning of a program to the end of the program
CPU Execution Time
  Counts only the amount of time that is effectively dedicated to *your* program
    Many other programs running on your machine at the same time (time slicing)
    Requires a profiling tool to assess (like gprof, for instance)
On a dedicated machine; i.e., a quiet machine, Wall Clock Time and CPU Execution Time should be identical
User time – the time spent processing instructions compiled out of code generated by the user or in libraries that are directly called by user code
System time – time spent in support of the user’s program but in instructions that were not generated out of code written by the user
  OS support: open file for writing/reading, throw an exception, etc.
Clock cycle: sets the pace at which the execution proceeds
  A constant value dictated by the frequency at which processor operates
[Patterson, 4th edition]→
Notes: In general: Program Execution Time is what you care about (end-to-end time to solution)

## Slide 39: The CPU Performance Equation
[Patterson, 4th edition]→
Three ingredients control the amount of time for execution of a program:
  Number of instructions that your program has (Instruction Count)
  Average number of “clock-cycles per instructions” (CPI)
  Clock Cycle Time
The CPU Performance Equation reads:
Alternatively, using the clock rate:
As repeatedly demonstrated in practice, reducing the Instruction Count (IC) often times leads to an increase in CPI. And the other way around.

## Slide 40: Big New Topic: Memory Aspects

## Slide 41: SRAM vs. DRAM: wrap-up
Order of the SRAM access time: 4 to 5 cycles (nanoseconds)
  Expensive but fast
  Transistor hog
  Needs no refresh
Order of the DRAM access time: 10s of cycles
  The information stored as a charge in a capacitor
  Less expensive but slow
  Requires one capacitor and one transistor, might have capacitor leak
  Higher capacity per unit area
  Needs refresh every 10-100 ms (a small overhead in memory access – around 0.1%)
  Sensitive to disturbances
Limit case: a 10X - 100X speedup
if you can work off the SRAM
[Rauber&Runger]→
 | Transistors per bit | Access Time | Persistent? | Sensitive? | Price | Applications
SRAM | 6 | 1X | Yes | No | 100X | Cache memories
DRAM | 1 | 10s X | No | Yes | 1X | Main Memory
 | SRAM | DRAM | Flash
Speed | Very fast | Fast | Very slow
Density | Low | High | Very high
Power | Low | High | Very low
Refresh | No | Yes | No
Retention | Volatile | Volatile | Non-volatile
Mechanism | Bi-stable Latch | Capacitor | Fowler-Nordheim tunneling
Notes: [Rauber&Runger]→ Typical access times are 0.5–2.5 ns (ns = nanoseconds = 10−9 seconds) compared to 50–70 ns for DRAM (values from 2008 [84])
From Rochester (http://www.cs.rochester.edu/~sandhya/csc252/lectures/lecture-storage.pdf):
Key features
– RAM is packaged as a chip.
– Basic storage unit is a cell (one bit per cell).
– Multiple RAM chips form a memory.
• Static RAM (SRAM)
– Each cell stores bit with a six-transistor circuit.
– Retains value indefinitely, as long as it is kept powered.
– Relatively insensitive to disturbances such as electrical noise.
– Faster and more expensive than DRAM.
• Dynamic RAM (DRAM)
– Each cell stores bit with a capacitor and transistor.
– Value must be refreshed every 10-100 ms.
– Sensitive to disturbances.
– Slower and cheaper than SRAM.

## Slide 42: New Topic: The Memory Hierarchy
Observation 1: over time, speed of data processing increased faster than speed at which we could bring over data to be processed
Observation 2: the bigger the memory used to store data, the longer it takes to find/access an entry therein
  Compromise between size and speed of access
Consequences of Observations 1 & 2: a hierarchy of memories has emerged
Managing memory hierarchy not trivial → a dedicated hardware asset called MMU (memory management unit) handling this task
  MMU’s purview: virtual memory management, cache control, memory protection, bus arbitration, etc.
Compromise:
  Have some SRAM on-chip, making up what is called the “cache”
  Have a lot of inexpensive DRAM off-chip, making up the “main memory”
    This is what people have in mind when they ask you “How much memory does your system have”?
In our code, we hope to have low “average memory access time” by hitting the cache repeatedly instead of taking costly trips to main memory
All caches are typically on the chip and are SRAM

## Slide 43: Memory Hierarchy
Moving on to talk about caches
The collection of all registers is called “the register file”

## Slide 44: Cache Memories
Cache memories are small, fast, on-chip SRAM-based memories
  Purpose: to store close to the CU/ALU frequently accessed blocks of main (aka “system”) memory
Schematic of chip’s datapath (chip=datapath + CU), and where cache fits in the big pic:
Main
memory
I/O
bridge
Bus interface
ALU
Register file
The DATAPATH
System bus
Memory bus
Cache
memory
[Bryant and O‘Hallaron: CMU] →

## Slide 45: How Cache Comes into Play
All* read/write operations go through cache
Caches used to hold both data and instructions
  Data and instructions caches are in general different
    Intel: L1 DC (data cache) and L1 IC (instruction cache) have been distinct since about 1993
Main Memory
Cache
CPU Core
Bus

## Slide 46: Caches: Come In Two Flavors
Data caches feed processor with data manipulated during execution
  If processor would rely on data provided by main memory the execution would be pitifully slow
    “Processor Clock” much faster than the “Memory Clock”
      Caches alleviate the memory pressure – processors are data hungry
Instruction caches: used to store instructions
  Simpler to deal with compared to the data caches
    By and large, instruction use is much more predictable than data use

## Slide 47: Processor Clock vs. Memory Clock [important to understand]
Processor Clock: (look for the box )
  Dictates/defines the frequency at which Functional Units operate
Memory Clock:
  Dictates/defines the frequency used to move data into/out from main memory into cache
From RAM
To/From RAM

## Slide 48: Multiple Levels of Cache
Typically, commodity chips today have 3 cache levels
  (some chips have a fourth cache level, see previous slide)
Main Memory
L3 Cache
Bus
L2 Cache
L1 D$
CPU Core
L1 I$
Main Memory
Cache
CPU Core
Bus
Zoom in

## Slide 49: Example: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 7
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way assoc.
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way assoc.
  Access: 10 cycles
L3 unified cache:
  8 MB, 16-way assoc.
  Access: 40-75 cycles
Cache line size: 64 bytes for all caches.
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →

## Slide 50: The reason caches can [sometimes] make a difference: “Principle of Locality”
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  “Recently referenced items are likely to be referenced again in the near future”
  Example:
    A for loop with some variables inside the loop
    Variable sum referenced at each iteration
Spatial locality:
  “Items with nearby addresses tend to come into use together”
  A memory access pattern characterized by bursts of repeated requests for data that is physically located within the same memory region
  Example:
    Reference instructions in sequence
    Array abc elements accessed in succession (stride-1 reference pattern)
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →

## Slide 51: Matrix, stored in 2D format
The Memory
0
1
2
3
0
8
9
10
11
2
16
17
18
19
4
12
13
14
15
3
4
5
6
7
1
Matrix storage scheme:
“proper 2D”
999999
999998
999997
999996
250000
249999
Legend:
Boxes of this color used to show sequence of entries read for row-wise access of elements
Boxes of this color used to show sequence of entries read for column-wise access of elements
250,000th row
1st row
2nd row
Matrix dimensions
250,000 × 4
1 million elements

## Slide 52: Three observations related to our 2D and 3D examples
Observation 1: Final value for sum - stays the same (at least as far as we can tell)
  We’ll talk more about this when we do parallel computing w/ CUDA and then OpenMP
Observation 2: Difference between Debug vs Release builds
  3X to 4X speedup normal to see when going from debug to release (see also results on next slide)
Observation 3: Amount of time to get the result quite different
  Release mode build: the undesirable solution for 3D matrix is 30 times slower
    This is the case you see in practice – you build in release

## Slide 53: Observations on “Observation 1”
The fact that the results are the same is remarkable
Why remarkable?
  Finite precision arithmetic: addition loses its commutative and associative attributes
$ python
Python 3.9.12 (main, Apr 5 2022, 06:56:58)
[GCC 7.5.0] :: Anaconda, Inc. on linux
Type "help", "copyright", "credits" or "license" for more information.
>>> 0.001 + 1E20 - 1E20
0.0
>>> -1E20 + 1E20 + 0.001
0.001
>>>

## Slide 54: Observations on “Observation 3” (most important)
Q: What mechanism comes into play to yield a 30X speed gain?
A: The cache
  L1 cache: 4 cycles
  System memory access: 100-120 cycles

## Slide 55: The Lesson Learned
Fact: Wide gap in the speed of “using data” vs. “moving data”
  Using data: you do sin of that data, log, pow, add, subtract, etc. (processing the data)
  Moving data: getting your data from the system memory (64 GB/128/etc. GB that you have on your system)
Fact: The cache used to close the big speed gap
Trait of well-written programs: the programs leverage data/instruction locality
  Locality is what allows caches to come into play
  Locality necessary, but not sufficient (more later, “false sharing”)

## Slide 56: The Lesson Learned
Fact: Wide gap in the speed of “processing data” vs. “moving data”
  Processing data: on that data, you do operations such as sin, log, pow, add, subtract, etc.
  Moving data: getting your data from the system memory (64 GB/128/etc. GB of main memory)
Fact: The cache emerged as a way of managing the CPU vs. Memory speed gap
Trait of well-written programs: the programs leverage data/instruction locality
  Locality is what allows caches to assist you

## Slide 57: [Back to caches: The inner workings of caches] General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
The Cache
The Main Memory
Main Memory: Larger, slower, cheaper memory
(shown here as partitioned into “blocks” that are
mapped into cache lines)
Data copied in block-sized transfer units. Each block (such as block 10, for instance) typically holds 64 bytes of data (called cache line).
Smaller, faster, more expensive
memory can store a subset of
the main memory blocks
4
4
4
10
10
10
Everything handled in hardware. Invisible to programmer
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →
Notes: 10, or 9, or 3, etc. – these are cache line (or blocks). In main memory, called “a block”; in cache, called “a line”

## Slide 58: Cache Line (aka Cache Block)
When data is brought in cache because a piece of data is needed, the MMU brings more than just the needed piece of data
Bring more data than what absolutely necessary -- because penalty is not high for bringing more: wide buses, little extra cost in bringing more data than exactly what needed
Corollary: you will reduce the number of trips to main memory if you use multiple times data from a cache line
“cache line”
  Many systems have cache line of 64 Bytes (8 doubles OR 16 floats OR 16 ints OR 64 chars, etc.)
  Cache line size is the same for L1, L2, and L3 caches

## Slide 59: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!
Delivery to registers…
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →
Hit Rate: on average, how many out of 100 mem requests hit the cache? (we’ll talk about this again)

## Slide 60: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where Block b goes
Replacement policy: determines which block gets evicted (victim), should there be any freedom of choice
Delivery to registers…
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →

## Slide 61: Most common reasons for Cache Misses
Cold (compulsory) miss
  Happens when: cache is empty (e.g., beginning of the program, time slicing while having multiple programs in flight)
Capacity miss
  Happens when: Not enough space, working set is too large
    Example: the active part of main memory overwhelms in size what can be accommodated by the cache
      You are asking for more than what level can accommodate (fit)
Conflict miss
  Happens when: Enough space, but you have bad luck (lots of “conflicts”, as dictated by placement/replacement policy in place)
  Fact: In the memory hierarchy, the cache blocks at level map into a small subset of block positions at level
    Example (see previous slide): block at level must be placed in block () at level
  Conflict misses occur when the level cache is large enough, but multiple data objects all map to the same block in the level cache.
    Example (see previous slide): Referencing in this order blocks 0, 8, 0, 8, 0, 8, ... would miss every time (since )

## Slide 62: Cache Miss Classification, by Request Type
Cache read miss from an instruction cache: generally causes the most delay, because the processor, or at least the thread of execution, has to wait (stall) until the instruction is fetched from main memory
A cache read miss from a data cache: usually causes less delay (compared to instruction cache miss)
  OOOE: Instructions not dependent on the cache read (if any) can be issued and executed until the data is fetched from main memory and the stalled instructions can resume execution
  TLP: Another thread can be picked up for execution
A cache write miss to a data cache: generally causes the least delay, because the write can be queued and there are few limitations on the execution of subsequent instructions. The processor can continue unless the queue is full and then it has to stall for the write buffer to partially drain

## Slide 63: Placement & Replacement Policies
Direct mapping: cache structured as skinny skyscraper, with one apartment per story (E = 1)
  An “apartment” large enough to accommodate 64 folks (Bytes)
Associative, K-way: a certain number of floors (stories), each with K apartments
Fully associative cache: apartment complex with ground level only (ranch)

## Slide 64: Placement & Replacement Policies: further discussion
Direct map (the tall skinny skyscraper)
  Pros: very fast to find if in cache or not
  Cons: sometimes, you’ll have to evict a cache line that sees a lot of use (no freedom at all in the placement policy)
K-way associative (Hilton Garden Inn)
  Decent compromise:
    You don’t have to search too many “apartments” at a floor level for a matching tag
    It yields a reasonably decent replacement policy – you have K options to choose from
Fully associative (the ranch)
  Pros: you have full control which old cache line you want to kick out (lots of freedom for replacement policy)
  Cons:
    Higher overhead to find what you’re looking for (data can be anywhere in cache)
    Higher overhead to decide whom to evict (the “victim”) – in case you don’t have a hit

## Slide 65: The BEST rule: The “folks in an apartment building” metaphor
The total number T of folks in the building depends on
  How many stories/floors in the building (S) -- The number of “Sets” that make up the cache
  How many apartment per floor level (E) -- The number of cache lines in a set, typically E = 2^n
  How many folks in an apartment (B) -- Number of bytes in a cache line, typically B = 64
Total number of folks in the building:
t bits
s bits
b bits
Memory address (either 32 or 64 bits)
tag
set
index
block
offset
NOTE: Think of the “set index” as which floor in the building

## Slide 66: General Cache Organization (B, E, S)
E = 2e lines per set
S = 2s sets
a “cache Set”
a “cache Element” (it wraps inside a cache line; an element belongs to a set)
0
1
2
B-1
tag
v
B = 2b bytes of data per cache block (cache line)
Cache size:
B x E x S=T data bytes
valid bit
[Bryant and O‘Hallaron: CMU] →
How a “cache Element” is organized

## Slide 67: We’ve done memory reads. What about writes?
Multiple copies of data exist stored in different places and at the same time:
  L1, L2, L3, Main Memory, Secondary Memory (Disk)
How should a write-hit be handled?
  Write-through (write immediately to main memory as well)
  Write-back (defer write to memory until replacement of line)
    Need a dirty bit (indicate whether line different from memory or not)
How should a write-miss be handled?
  Write-allocate (write to next level down memory, but also update this cache level)
    Good if more writes to the location follow; i.e., if locality is good
  No-write-allocate (writes straight to next level down memory, do not load into this cache level)
Typical combos met in practice:
  Write-back + Write-allocate ← more common
  Write-through + No-write-allocate

## Slide 68: Cache performance metrics [a nomenclature matter]
Miss Rate
  Defined as Miss Rate = 1 – Hit Rate (note that we defined the “Hit Rate” concept before)
  Miss rate represents the fraction of memory references that are not found in cache
    3 - 10% for L1
    Can be quite small (e.g., < 1%) for L2, depending on size, nature of problem you run, etc.
Hit Time
  Time to deliver a line in the cache into a register of the processor
    Includes time to determine whether the line is in the cache
  Typical numbers:
    4 clock cycles for L1
    10 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    Typically 50-200 cycles for main memory (Trend: slightly increasing)
[Bryant and O‘Hallaron: CMU] →

## Slide 69
People talk about miss rate, and not hit rate
Weird math: Although 97 and 99 are close, is 99% hit rate twice as costly as 97% hit rate???
  Assumptions, for back of the envelope calculation: a) cache hit time of 1 cycle b) miss penalty of 100 cycles
  97% vs 99% hit rate: Access cost for 100 mem operations
  97% hit rate:
  99% hit rate:
You’d think that 97% is as good as 99%. It’s not…
  This is why “miss rate” is used instead of “hit rate”: 1% miss rate vs. 3% miss rate
[Bryant and O‘Hallaron: CMU] →
People Talk about Miss Rate, Not Hit Rate

## Slide 70: Writing Cache Friendly Code: Rules of Thumb
Basic facts:
  You have no direct control over what data gets cached
  You can perhaps ensure your code is “local” (spatially and/or temporally)
Make the common case go fast
  Focus on the inner loops of the “heavy” functions
Try to have cache-friendly code in the inner loops
  Repeated references to same variables are good (temporal locality)
  “stride of one” reference patterns are good (spatial locality)
[Bryant and O‘Hallaron: CMU] →

## Slide 71: The “Memory Mountain” Experiment
Memory mountain: Measures read-throughput as a function of spatial and temporal locality
  Compact way to characterize memory system performance
Read throughput (or “read bandwidth”)
  Number of bytes read from main memory per second (MB/s)
“effective bandwidth”: computed by dividing amount of data moved to solve the problem (in Bytes) to the amount of time required to finish the execution (in seconds)
NOTE: “effective bandwidth” is smaller than or equal to the bandwidth
  A lot of data might be moved, but only a small subset might be used towards solving the problem
    Happens when you violate the principle of locality
  The “effective bandwidth” computed based on the amount of Bytes in the “small subset”

## Slide 72: New Topic: Virtual Memory

## Slide 73: Virtual vs. Physical Memory
Virtual memory: a dally and quaint fictitious space of 232 addresses (on 32 bit architectures) in which a process sees its data being placed, the instructions stored, etc. This is what the compiler deals with
Physical memory: a busy place that hosts at the same time data and instructions associated with tens of applications running on the system
The Virtual Memory paradigm allows:
  Running programs that manipulate more data than storage physically available in the main memory
  Running multiple programs seemingly “simultaneously” (multi-tasking)
  Transparent and unitary handling of main memory and secondary storage (hard disk / solid state disk)
  Handling of memory fragmentation/segmentation insofar as the main memory is concerned
The Memory Management Unit (MMU) manages the Virtual Memory and can perform:
  Memory protection
  Cache control
  Bus arbitration

## Slide 74: The Virtual Memory: its anatomy
addresses (32 bit OS)
Notes: Ignore for the moment the messiness of the physical memory and concentrate on how the “pristine” layout of the virtual memory is seen by a process.
Each process partitions its virtual memory layout in several segments as shown here.
Nice discussion why BSS & DATA segments are needed is here: https://stackoverflow.com/questions/16557677/difference-between-data-section-and-the-bss-section-in-c

## Slide 75: Anatomy of the Stack
Function bar and associated stack frame
Notes: Reasons for the stack: you don’t know how many times a function is called. The function needs to place its data somewhere. It’s like a hidden malloc followed by a copying of the arguments (a and b, above) in this memory, which will also be hit by t1, t2, etc.
The stack is a segment of fixed size that is managed in a LIFO manner (push and pop).
Order of variables in stack is decided by compiler. Typically arrays are stored contiguously.
Note: stack also stores value of return address (from subroutine). This is a back-door that can be used by malicious programs to hijack execution: bar() above could try to write to initials[1000] in the hope to overwrite a return address for a function higher up in the call stack.

## Slide 76: Page Table [stored in main memory]: the mechanics of address translation
NOTE: not every virtual address is mapped to a physical memory address
  It’s more like a chunk of virtual addresses (called a page), is mapped to a chunk of physical addresses
    More precisely: A chunk is called a page (in virtual memory) and frame (in physical memory)
A virtual address split into two parts (another case of address splitting, like for caches, when we split 3 ways):
  The page number
  The offset in the page
Example below assumes a 32-bit OS with virtual pages of size bytes
[physical memory]
Notes: The virtual memory is split into pages.
The physical memory is split into frames.
This is for a 32-bit OS with virtual pages of 4096 bytes.
4096 = 2^12  need 12 bits to indicate the offset in the page.
(Note: unit of address resolution is 8 bits  a virtual page holds 4 KB)
The remaining 32-12 = 20 bits used to index into the Page Table to get the corresponding frame number (which is held in N bits)

## Slide 77: Anatomy of a Virtual Memory Address
A page of virtual memory is tied to a frame of physical memory
The size of a page (or frame, for that matter) is typically 4096 bytes
  Compare to 64 bytes, the size of a cache line (aka memory block)
4096=212 12 bits of the address are sufficient to relatively position each byte in a page
  Bits marked 0 through 11 on the previous slide
Physical Frame ID
Physical Frame ID
Physical Frame ID
Physical Frame ID
Physical Frame ID
Physical Frame ID

## Slide 78: The TLB [Translation Lookaside Buffer]
If you go to Page Table in main memory for each address translation this would be very costly
  One trip to translate address, one trip to actually fetch the data
There is a “cache” for the address translation process: TLB
  Translation Lookaside Buffer: holds the translation of a small collection of virtual page numbers into frame IDs
The Good: the TLB leads to a hit and allows for quick address translation
The Bad: TLB doesn’t have the required information cached and a trip to main memory in order; required to read the PT entry
The Ugly: on top of “Bad”, the requested frame not in main memory and a trip to secondary memory in order
  Called “page fault,” you’re hitting significant latency at this point
  “memory thrashing”: repeatedly hitting page faults, to the point where time wasted in handling page faults dominates all the rest
Notes: On page fault, the OS does the following:
data requested is located in secondary storage
request made for an entire (“surrounding”) frame to be brought over in main memory
room is made for the new frame as a virtual page (this may require evicting an existing one; e.g. using a LRU strategy)
the new frame is loaded in the virtual page
the PT is updated to reflect the change
control returns to process which is instructed to retry the instruction that led to a page fault

## Slide 79: Memory Access: The Big Picture, Includes Cache
A simplified version of how a memory request is serviced:
Notes: Note that the virtual memory mechanism allows looking at main memory as a “cache” for secondary storage.
Memory block  memory frame
Cache line (64 bytes)  virtual memory page (4096 bytes)
Cache miss  page fault
Note: page fault much more costly (secondary storage is even “farther” from RAM than RAM is to CPU)

## Slide 80: malloc vs. calloc: some ways in which they’re different
malloc:
  Allocates space in virtual memory
  Sets aside no space in physical memory
    Physical memory set aside only when needed
      (Delayed physical allocation, done upon “touch”)
      The Page Table not populated yet with values that are valid yet
calloc:
  Allocates space in virtual memory
  Sets aside also physical memory
  Physical memory initialized to a bunch of zeros
calloc takes longer than similar malloc call: physical mem actually provisioned and also set to zero
int * alloc_ints(size_t requested_count)
{
int * big_array;
big_array = (int *)calloc(requested_count, sizeof(int));
if (big_array == NULL) {
printf(“can’t allocate %d ints : %m\n”, requested_count);
return NULL;
}
/* big_array[0] through big_array[requested_count-1] are
* valid and zeroed. */
return big_array;
}

## Slide 81: The Clean/Dirty Bit & the concept of Page Fault
Bit is “clean”: two conditions need to happen for the bit to be clean
  The frame that the page gets translated into has been loaded in main memory
  Since last translation, that very frame has not been associated with other virtual page
Bit is “dirty”:
  We called this “page fault”, costly scenario to handle
  The OS will look for the needed frame on disk (secondary memory)
    The way you can think about it: the RAM (main mem) is the cache of the hard-disk (secondary mem)
      If bit in Page Table is dirty, the translation refers to address in secondary memory, not in main memory
  NOTE: A lot of such bits will be dirty when you start the execution of a program
    Your data & instructions are not in memory

## Slide 82: [New Short Topic] The size of the frame/page
Refresher: a memory page, or virtual page, is a fixed-length contiguous block of virtual memory, described by a single entry in the Page Table
The frame is the fysical (or physical) counterpart of a virtual page
Typically, size of page is 4 KB but can be of 1024 KB for certain applications
  Example: working with very large data sets (big data)
Large page size,
  Pros: less TLB pressure -- fewer pages to blanket the virtual memory means fewer entries in the Page Table, which means
    Fewer values that compete for storage in the TLB cache. More TLB hits: faster program
    [not that big of a deal] The size of the Page Table is smaller – less memory needed to store it
  Cons: might lead to wasteful use of physical memory
    Bad for the other processes running next to yours in time-sharing (multi-tasking)
      The OS might start recording lots of page faults

## Slide 83: Parallel computing: why, and why now?

## Slide 84: Main causes for sequential computing speed stalling
Memory Wall
  The growing disparity of speed between CPU and memory outside the chip
  Due to latency and limited communication bandwidth beyond chip boundaries
  The trend: ever growing caches to improve average memory reference time to fetch or write instructions or data
  Memory-wise, you may or may not be at top speed for your memory
    Effective bandwidth==Nominal bandwidth: you move lots of data - ok, fact of life, some applications are just like that
    Effective bandwidth < Nominal bandwidth: you bring a block of data, use little of it, and ask for data from a different block
Instruction Level Parallelism (ILP) Wall
  ILP elicits very complex microarchitecture
Power Wall
  Power dissipation related to the clock frequency and feature length
    Consequence (the wall): clock rates are limited to some threshold value
  Significant increase in clock speed without heroic/expensive cooling not possible -- Chips would simply melt
  Power, and not manufacturing, limits traditional general purpose microarchitecture improvements
Not necessarily walls, but increasingly steep hills to climb
Notes: Predicted in 2000:

## Slide 85: Memory Latencies [typical server and mobile computers]
Courtesy of Elsevier, Computer Architecture, Hennessey and Patterson, fifth edition
Server
Mobile
CPU
Registers
Notes: Hammad: in the fifth edition of the book embedded/mobile have their own diagram

## Slide 86: Memory Latency vs. Memory Bandwidth [1/2]
Latency [in our context]: how much time it takes a packet of data to get from one designated point to another
  Measured in seconds, also called “lag”
  The utility “ping” in Linux measures the latency of a network
  For memory transactions: send 32 bits to destination and back, measure how much time it takes gives you latency
Bandwidth: how much data can be transferred per second
  You can talk about bandwidth for memory but also for a network (Ethernet, Infiniband, modem, DSL, etc.)
Improving Latency and Bandwidth
  Mostly the job of folks in Electrical Engineering
  Once in a while, Materials Science colleagues deliver a breakthrough
  Promising technology: optic networks; layered memory on top of chip; etc.

## Slide 87: Memory Latency vs. Memory Bandwidth [2/2]
Memory Access Latency more challenging to improve as opposed to improving Memory Bandwidth
Improving Bandwidth: doable, add more “pipes”
  Requires more pins that come out of the chip for DRAM, for instance
  Adding more pins is not simple – very crowded real estate plus the technology is tricky
Improving Latency: no quick way to improve things here
Analogy:
  If you carry commuters with a train, add more cars to a train to increase bandwidth
  Improving latency requires the construction of high speed trains (expensive/complex)
IMPORTANT NOTE: Improving bandwidth is challenging, but doable; improving latency is very tough

## Slide 88: The ILP Wall
Dedicated hardware speculatively executes future instructions before the results of current instructions are known, while providing hardware safeguards to prevent the errors that might be caused by out of order execution
Branches must be “guessed” to decide what instructions to execute simultaneously
  If you guessed wrong, you throw away that part of the result
Data dependencies may prevent successive instructions from executing in parallel, even if there are no branches
Predicting the future comes at the cost of microarchitecture complexity and power cost

## Slide 89: Parallel computing: The Ox vs. Chickens Analogy
Ox: one powerful CPU core, running at high frequency, large cache to hide memory latency
Chicken: many meagre processors, running at lower frequency, not much cache or CU brain
  Requires other ways to hide memory latency
Few were eating chicken two decades ago. Very popular now
“If you were plowing a field, which would you rather use: Two strong oxen or 1024 chickens?” [Seymour Cray]

## Slide 90: The Fermi Architecture [ Schematic of a NVIDIA Stream Multiprocessor (SM)]
Late 2009, early 2010
40 nm technology
Three billion transistors
512 Scalar Processors (SPs), or “shaders”
  These are the chickens
L1 cache
L2 cache
6 GB of global memory
Operates at low clock rate
High bandwidth (for 2010, 200 GB/s)

## Slide 91: A Fermi SM (Streaming Multiprocessor (SM); one of 16)
Not a whole lot of brain here, compared to CPU.
Specifically, no orange boxes, which have to do with ILP.
[NOTE: color code is the same for SM & CPU]
Fermi Stream Multiprocessor

## Slide 92: Fermi: 30,000 feet perspective, the entire chip
Lots of ALU (green), not much of CU (orange)
Explains why GPUs are fast for high arithmetic intensity applications
Arithmetic intensity: high when many operations performed per byte of data

## Slide 93: The CPU and GPU: showing their true colors
The GPU is specialized for compute-intensive, highly data parallel computation (owing to its graphics rendering origin)
  More transistors devoted to data processing rather than data caching and control flow
  Where are GPUs good: high arithmetic intensity (the ratio between arithmetic operations and memory operations)
The video game industry exerts strong economic pressure that pushes things forward in GPU computing
DRAM
Cache
ALU
Control
ALU
ALU
ALU
DRAM
CPU
GPU

## Slide 94: [New Topic] Flynn’s Taxonomy of Architectures [Moving away from hardware; moving into software aspects]
Classification based on how instructions are executed in relation to data
  PU = Processing Unit
SISD - Single Instruction/Single Data
SIMD - Single Instruction/Multiple Data
  GPUs
MISD - Multiple Instruction/Single Data
MIMD - Multiple Instruction/Multiple Data
  Almost all our desktop/laptop chips
  Each PU is free to do as it pleases
  Either shared memory or distributed memory

## Slide 95: Algorithmic vs. Intrinsic Scaling
Algorithmic Scaling of a solution algorithm
  Strictly about a mathematical solution algorithm
  Expresses how the algorithm scales with the problem size
  Examples:
    Naïve implementation of the N-body problem scales like O(N2), where N is the number of bodies
      Sophisticated algorithms scale like O(N logN)
    Gauss elimination for matrix factorization scales like the cube of the number of unknowns in your linear system
Implementation Scaling of a solution on a certain architecture
  Intrinsic Scaling: how the execution time changes with an increase in the size of the problem
  Strong Scaling: how the execution time changes when you increase the processing resources
  Weak Scaling: how the execution time changes when you increase the problem size but also the processing resources in a way that basically keeps the ratio of “problem size/processor” constant

## Slide 96: Scaling, Closing Remarks
Important: Is the Intrinsic Scaling similar to the Algorithmic Scaling?
  If Intrinsic Scaling significantly worse than Algorithmic Scaling then probably memory transactions are dominating the implementation
If the problem doesn’t scale, it can be an interplay of several factors
  The intrinsic nature of the problem at hand
  The attributes (organization) of the underlying hardware
  The algorithm used to solve the problem; i.e., the parallelism it exposes

## Slide 97: GPU Computing with CUDA

## Slide 98: Bandwidth in a CPU-GPU System [high speed requires high bandwidth]
98
System Memory
(256 GB)
GPU SMs
120
GB/s
16-32 GB/s
1555
GB/s
CPU Core
Cache L1: 32 KB
L2: 256 KB
L3: 45 MB (shared)
6GB/s
Infiniband to Next Node
Latency:
High
[4-6 us]
Latency:
Medium
Latency:
Medium Low
Latency:
Very Low
Latency:
Rel.Low
NOTE: The width of the black lines is proportional to the bandwidth.
GPU Memory
(40 GB)
Notes: 98
Hammad – GPU numbers are for a Pascal P100, PCI numbers are for PCIe3
Infiniband is assuming mellanox results from here: http://www.mellanox.com/page/performance_infiniband
CPU memory numbers are for a E7 8890v3 http://ark.intel.com/products/84685/Intel-Xeon-Processor-E7-8890-v3-45M-Cache-2_50-GHz
CPU cache numbers are an average between expected L1 and L3 cache performance (not exact but approximate)

## Slide 99: Coarse Grain vs. Fine Grain Parallelism
#pragma omp parallel sections
{
#pragma omp section
a = alice();
#pragma omp section
b = bob();
#pragma omp section
k = kate();
}
double s = boss(a, b);
double result = bigboss(s,k);
[IOMPP]→
alice
bob
boss
bigboss
kate
Coarse Grain
Fine Grain
DRAM
GPU
Cache
ALU
Control
ALU
ALU
ALU
DRAM
CPU

## Slide 100: Coarse Grain vs. Fine Grain Parallelism
Coarse grain parallelism (good for CPUs)
  Few tasks
  Tasks are heterogeneous
  Tasks are in general complex, lots of control flow
  Example: baking a cake, making coffee, broiling fish – all at the same time
Fine grain parallelism (very good for GPU, ok for CPU)
  Many, many tasks
  Tasks are basically identical
  Tasks are in general pretty straightforward, lots of math, not much control flow
  Example application: computer graphics – lots of pixels to deal with
    “shaders” – deal with one pixel at a time

## Slide 101: GPGPU Computing [General Purpose GPU Computing]: how carried out
GPUs had high bandwidths
The idea is to use the GPU as a co-processor
  Farm out big parallel jobs to the GPU
  CPU stays busy with the control of the execution and “corner” tasks
  Data moved down into the GPU, and then results fetched back (idea works ok when data transfer overhead overshadowed by the number crunching done using that data)
NOTE: up until 4 years ago the “Data moved down into the GPU” was the responsibility of the programmer. Not the case anymore as of recently (from Pascal on).
IMPORTANT: for now, we’ll still manage CPUGPU data movement. Revisit issue in six lectures
Notes: People realized quickly that GPUs can be used for more, beyond graphics.
GPGPU – first utilization of GPUs for General Purpose.
The idea was to “hijack” shader programs to make them do other useful computations
very awkward and difficult
limited (e.g. communication limited between pixels: only gather, but no scatter – could only write to 1 pixel, no support for integer arithmetic)

## Slide 102: CUDA Programming Model: GPU as a Highly Multithreaded Coprocessor
CUDA: “Compute Unified Device Architecture”
The GPU is viewed as a compute device that:
  Is a co-processor to the CPU or host
  Has its own memory (device memory, in CUDA parlance)
  Runs many threads in parallel
Data-parallel portions of an app. run on the device as kernels executed in parallel by many threads
Differences between GPU and CPU threads
  GPU threads are extremely lightweight
    Very little creation overhead
  GPU needs 1000s of threads for full efficiency
    Multi-core CPU needs only a few heavy ones
The basic rule: the CUDA Driver API is backward, but not forward compatible
  The functionality in later versions increased, was not there in previous versions
Notes: The model is:
host copies data to device
host launches a computation (kernel) on the device
host copies back data from device

## Slide 103: The CUDA Execution Model
This is how your C code looks like
This is how the code gets executed on the hardware in heterogeneous computing. GPU calls are asynchronous…
Execution of Kernel0
Execution of Kernel1
Notes: NOTE: Execution on the GPU is ORDERED!
You can COUNT on this + global memory PERSISTENT  split work in multiple kernels.
Asynchronous: Important because you can do useful work on the CPU while the GPU works
Beware of this when timing kernel execution – see later
If you really need to make the CPU wait for the GPU, use cudaDeviceSynchronize(), which enforces the CPU to wait until all preceding commands in all streams of all host threads have completed.
Copying data from device back to host is a synchronization point in that stream: cudaMemcpy is synchronous.
There are asynchronous versions of cudaMemcpy

## Slide 104: The CUDA Execution Model
Data needs to be copied into GPU device memory and the results need to be fetched back
  This happens over a PCI-Express 3.0/4.0 connection
  Can also happen over NVLink (5-12 times faster than PCI-E)
    NVLink: Available on one Euler node only
IMPORTANT:
  For GPU computing to pay off, the data transfer overhead should be overshadowed by the GPU number crunching that draws on that data
The CUDA kernel calls and copying to/from GPU are managed by the CUDA runtime in a separate stream associated w/ the GPU execution
Notes: The GPU has actually 3 engines which can be used simultaneously.
We will not get into this more advanced topic (streams)
GPU cards support multiple streams so that you can execute in a stream and copy data in another stream. The streams are independent, so you must explicitly synchronize. Working with a single stream (0), synchronization at copying time is automatic.

## Slide 105: The concept of “CUDA host stream”
“CUDA host stream”: it has nothing to do with the SM (Stream Multiprocessor), which is a hardware thing
The CUDA runtime places all calls that invoke the GPU in a stream (i.e., ordered collection) of calls
    This stream is a FIFO (first-in-first-out) stream
      In example of two slides ago, Kernel1 will only be called once Kernel0 finished execution
  Important: there is an a-synchronicity between host and device
    Host: minds its business, continuing execution right away after launching a kernel
    Device: minds its business, taking on the next task in the sequence of tasks in the stream
Notes: The GPU has actually 3 engines which can be used simultaneously.
We will not get into this more advanced topic (streams)
GPU cards support multiple streams so that you can execute in a stream and copy data in another stream. The streams are independent, so you must explicitly synchronize. Working with a single stream (0), synchronization at copying time is automatic.

## Slide 106: Further comments, on the “asynchronous” aspect of GPU computing
  Caveat to a-synchronicity
    There are implicit synchronization points: A H2D or D2H memory data copy cannot take place (stalls the host) until all other CUDA operations in the stream have completed
  You can even force everything to be synchronous during the execution of the code
    Simply set CUDA_LAUNCH_BLOCKING environment variable to 1.
  If you force kernel calls to be synchronous, you lose the opportunity to do something on the host while the device is busy running your kernel
Notes: The GPU has actually 3 engines which can be used simultaneously.
We will not get into this more advanced topic (streams)
GPU cards support multiple streams so that you can execute in a stream and copy data in another stream. The streams are independent, so you must explicitly synchronize. Working with a single stream (0), synchronization at copying time is automatic.

## Slide 107: More specifics: GPU operations that are asynchronous
The following calls made on the host return the control to host right away
  CUDA kernel launches
  CUDA memory copies within a single device's memory
    On the host, you ask the GPU to copy bytes from the GPU’s device memory to some other GPU mem location
  CUDA memory copies from host to device of a memory block of 64 KB or less
  CUDA memory copies performed by functions that are suffixed with Async
  CUDA “memory set” function calls

## Slide 108: The CUDA Execution Model: Three Opportunities for Asynchronous Execution
Three opportunities, listed in increasing order of use/engagement complexity
  Opportunity 1: The GPU and CPU work in asynchronous mode
    The CPU moves on right away after a kernel launch
    The GPU works at the same time the CPU works
  Opportunity 2: the GPU has three engines that can work at the same time
    copy-in engine + copy-out engine + execution engine
    More later (when we talk about streams)
  Opportunity 3: Multiple GPUs can work at the same time on one host
Notes: The GPU has actually 3 engines which can be used simultaneously.
We will not get into this more advanced topic (streams)
GPU cards support multiple streams so that you can execute in a stream and copy data in another stream. The streams are independent, so you must explicitly synchronize. Working with a single stream (0), synchronization at copying time is automatic.

## Slide 109: CUDA Function Declarations: (the “C with extensions” part)
 | Executed on the: | Only callable from the:
__device__ float myDeviceFunc() | device | device
__global__ void myKernelFunc() | device | host
__host__ float myHostFunc() | host | host
__global__ defines a kernel function, launched by host, executed on the device
  Must return void
NOTE: can combine __device__ with __host__
See CUDA Reference Manual http://docs.nvidia.com/cuda/cuda-c-programming-guide/index.html
Notes: Can combine: __device__ __host__

## Slide 110: GPU Execution Configuration

## Slide 111: [New Topic] The concept of Execution Configuration
__global__ void kernelFoo(...); // declaration
dim3 DimGrid(100, 50); // 2D grid structure, w/ total of 5000 thread blocks
dim3 DimBlock(4, 8, 8); // 3D block structure, with 256 threads per block
kernelFoo<<< DimGrid, DimBlock>>>(...your arg list comes here…);
A kernel function must be called with an execution configuration:
Threads in each block:
  The threads can be organized as a 3D structure (x,y,z)
  Maximum x- or y-dimension of a block is 1024
  Maximum z-dimension of a block is 64
  The maximum number of threads in each block is 1024
There is a limitation on the number of blocks in a grid:
  The grid of blocks can be organized as a 3D structure: max of 231-1 by 65,535 by 65,535 grid of blocks
Notes: How many threads do you want to use?
Difference with an OpenMP parallel for loop (forward reference)
on CPU you typically use as many threads as (virtual) cores you have
on a GPU you launch many more threads than SPs!
if you have a loop with 1 million iterations, those will be divided into 8 chunks on CPU
on a GPU you launch 1 million threads
You must divide the threads into blocks  these are executed by one SM (quantum of GPU scalability)
Max. number threads / block = 1024

## Slide 112: Important slide: a “block of threads” gets mapped to a SM
The concept of block is important since the “block of threads” represents the entity that gets executed by an SM
An SM can in some cases execute more than one block at the same time

## Slide 113: More on the Execution Configuration
Bottom line: max number of threads a kernel can be invoked with
Max count: about 9.444732965739290e+21 threads can execute a kernel
What if you want more threads to execute that kernel?
  You call the kernel again
Putting things in perspective:
  The kernel is executed by the threads you specify via your execution configuration setup
Max number of blocks in x-direction
Max number of blocks in y-direction
Max number of blocks in z-direction
Max number of threads in a block
Notes: Discuss 1-D, 2-D, 3-D configurations.
As of compute capability 5.x:
Maximum number of resident blocks per multiprocessor: 32
Maximum number of resident warps per multiprocessor: 64
Maximum number of resident threads per multiprocessor: 2048
Question: what do you do when you have more threads than possible? Launch multiple kernels!

## Slide 114: Block and Thread Index (Idx)
Threads and blocks have indices
  Used by each thread the decide what data to work on (more later)
  Block Index: a triplet of uint
  Thread Index: a triplet of uint
Why this 3D layout?
  Simplifies memory addressing when processing multidimensional data
    Handling matrices
    Solving PDEs on 3D subdomains
    …
Device
Grid 1
Block
(0, 0)
Block
(1, 0)
Block
(2, 0)
Block
(0, 1)
Block
(1, 1)
Block
(2, 1)
Block (1, 1)
Thread
(0, 1)
Thread
(1, 1)
Thread
(2, 1)
Thread
(3, 1)
Thread
(4, 1)
Thread
(0, 2)
Thread
(1, 2)
Thread
(2, 2)
Thread
(3, 2)
Thread
(4, 2)
Thread
(0, 0)
Thread
(1, 0)
Thread
(2, 0)
Thread
(3, 0)
Thread
(4, 0)
[NVIDIA]
Notes: A block is a collection of threads that can cooperate with each other by:
Synchronizing their execution
Efficiently sharing data through a low-latency shared memory
Each thread must know what piece of data it’s working on  must be able to “differentiate” itself from other threads in the same block or in a different block
Exercise:
How was the grid defined here (how many dimensions, how many blocks in each direction)?
How was a block defined?

## Slide 115: A couple (not all) of the built-in CUDA variables [Critical in supporting the SIMD parallel computing paradigm]
Each thread can find out the grid and block dimensions and its block index and thread index
  This info used to figure out what work the thread needs to do
Each thread when executing a kernel has access to the following read-only built-in variables
  threadIdx (uint3) – contains the thread index within a block
  blockDim (dim3) – contains the dimension of the block
  blockIdx (uint3) – contains the block index within the grid
  gridDim (dim3) – contains the dimension of the grid
  [ warpSize (uint) – provides warp size, we’ll talk about this later… ]
Notes: dim3  unspecified dimensions are initialized to 1 (not zero!)
warpSize  not used directly by CUDA code

## Slide 116: Matrix Multiplication Example - Device-side Kernel Function
// Matrix multiplication kernel – thread specification
__global__ void MatrixMulKernel(Matrix M, Matrix N, Matrix P) {
// 2D Thread Index; computing P[ty][tx]…
int tx = threadIdx.x;
int ty = threadIdx.y;
// Pvalue will end up storing the value of P[ty][tx].
// That is, P.elements[ty * P. width + tx] = Pvalue
float Pvalue = 0;
for (int k = 0; k < M.width; ++k) {
float Melement = M.elements[ty * M.width + k];
float Nelement = N.elements[k * N. width + tx];
Pvalue += Melement * Nelement;
}
// Write matrix to device memory; each thread one element
P.elements[ty * P. width + tx] = Pvalue;
}
M
N
P
WIDTH
WIDTH
WIDTH
WIDTH
tx
ty
Note: Pvalue is a local value; stored in a register. Access global memory once at the very end
Notes: Discuss why we have the local variable Pvalue
if we updated directly into the desired entry of P, we would make trips to global memory at each iteration
Pvalue declared here is local (and stored in a register)
we make a single trip to global memory to deposit the aggregate Pvalue
Note: a similar “trick” used in CPU code. There it has to do with not trashing the cache.

## Slide 117: Putting things in perspective
if (whichEntry < size) is needed to prevent out of bounds indexing
GPU computing: in general, one uses as many threads as data items/tasks present
  This replaces the purpose in life of the “for” loop
  Number of threads & blocks is established at run-time
Thus, in many cases, the rule is Number of threads = Number of data items (or tasks)
  You’ll have to come up with a rule to match a thread to data item that this thread needs to process
Understanding what thread does what job: very common source of errors in GPU computing
  This issue never fails to deliver (frustration)
  :-(
Notes: RECALL: make sure you do not access outside of bounds.
Always, check the thread ID against the data size.
Mapping threads <-> work is a recurring theme in CUDA programming. Important to do it right! Frustrating arithmetic and logic.

## Slide 118: Pad a Matrix for Overshooting
1493 entries in 1D array
Block 0: 512 threads
Block 1: 512 threads
Block 2: 512 threads
Block 16 by 16
Block 16 by 16
Block 16 by 16
Block 16 by 16
Block 16 by 16
Block 16 by 16
Block 16 by 16
Block 16 by 16
Block 16 by 16
Block 16 by 16
Block 16 by 16
Block 16 by 16
1D problem
Here’s what can happen in a 2D problem:
You are overshooting here
You are overshooting here as well
You are overshooting here, some threads do no work

## Slide 119: Array Indexing Demo: The multi-block case
When working w/ multiple blocks – you will likely be using more than just threadIdx.x
  Consider indexing into an 1D array, one thread accessing one element
  Assume you have M=8 threads per block and the array is 32 entries long
With M threads per 1D CUDA block, the array index that a thread works on is:
int index = threadIdx.x + blockIdx.x * M;
0
1
7
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
threadIdx.x
threadIdx.x
threadIdx.x
threadIdx.x
blockIdx.x = 0
blockIdx.x = 1
blockIdx.x = 2
blockIdx.x = 3
[NVIDIA]→
[Important to grasp: shows thread-to-task mapping]
Notes: Made up example, where a block can only have 8 threads, but we want to process an array with 32 entries.
0 <= threadIdx.x <= 7
What thread works on entry 21?
Identical to finding offset in 1-dimensional storage of a 2-dimensional matrix:
int index = x + width * y;

## Slide 120: Recurring Theme in CUDA Programming [summarizing previous discussion, started after CUDA Example]
Imagine you are one of many threads; you have your thread index & block index
Two things need to be addressed
  You need to figure out the work, or the job, you need to take care of
    Just like we did on previous slide, where thread 5 in block 2 realized it needed to work on entry 21
  You have to make sure you actually need to do that work
    In many problems there are threads that need not do any work
    Example: you launch 2 blocks with 512 threads; your array is only 1000 elements long; 24 threads at the end might do nothing
      “24 threads at the end might do nothing” – depending on the implementation

## Slide 121
Execution Scheduling Issues
Notes: Understanding execution scheduling is important for performance (effectively using the hardware).
Knowing the underlying hardware is also important on the CPU (e.g. being aware of caching – as we will see in the OpenMP section). However, the compiler and tool development on the GPU is much more recent and more is left to the developer.

## Slide 122: High-level Perspective
There are two schedulers at work in GPU computing
  A device-level scheduler: assigns one [more] block to an SM that signal that it has “excess capacity”
    Once a block is picked up for execution by one SM, the block does not leave that SM before all threads in that block finish executing the kernel
    Once a block is finished & retired, only then can another block land for execution on that SM
      The Device-Level Scheduler dispatches a block of threads to an SM that indicates that it has excess capacity
    This explains why it’s good to have many SMs in your GPU
      The more expensive the GPU, the more SMs it has (just like a CPU having more cores)
  An SM-level scheduler: schedules the execution of the threads in a block onto the SM functional units
    This is the more interesting scheduler
Notes: We’ll talk more about the SM-level scheduler as it is more interesting and important

## Slide 123: Device-Level Scheduler
This is the first levels of scheduling:
  For running [desirably] a large number of blocks (thousands) on a relatively small number of SMs
  There are perhaps tens of thousands of blocks that will eventually get executed in 108 SMs (on an A100)
Thread Blocks are distributed to the SMs
  Potentially more than one block per SM
As a Thread Block completes kernel execution on an SM, resources on that SM are freed
  Device level scheduler can launch next block in line
Limits, for resident blocks/SM:
  32 blocks on the Pascal SM, Volta SM, and Ampere SM
Another hard limit: no more than 2048 threads can be hosted on an SM (no matter how many blocks the threads are associated with/coming from)
Host
Kernel 1
Kernel 2
Device
Grid 1
Block
(0, 0)
Block
(1, 0)
Block
(2, 0)
Block
(0, 1)
Block
(1, 1)
Block
(2, 1)
Grid 2
Block (1, 1)
Thread
(0, 1)
Thread
(1, 1)
Thread
(2, 1)
Thread
(3, 1)
Thread
(4, 1)
Thread
(0, 2)
Thread
(1, 2)
Thread
(2, 2)
Thread
(3, 2)
Thread
(4, 2)
Thread
(0, 0)
Thread
(1, 0)
Thread
(2, 0)
Thread
(3, 0)
Thread
(4, 0)
Notes: Device-level schedules blocks for execution.
You cannot rely on order of block execution or assignment of blocks over SMs.
You can have 8 (Fermi) or 16 (Kepler) or 32 (recent) blocks resident on an SM

## Slide 124: SM-Level Schedulers
Each block of threads divided in 32-thread warps
  “32”: selected by NVIDIA, programmer has no say
  Warp: A group of 32 threads of consecutive IDs
Warps are the basic scheduling unit on the SM
Limit, number of resident warps on an SM: 64
  64: on Kepler, Maxwell, Pascal, Volta, Ampere (i.e., 2048 resident threads)
  48: on Fermi (i.e., 1536 resident threads)
  32: on Tesla (i.e., 1024 resident threads)
…
t0 t1 t2 … t31
…
…
t0 t1 t2 … t31
…
Warps of Block 1
Warps of Block 2
SP
SP
SP
124
Notes: Assume 2 blocks with 256 threads each.
So you have 512 threads that must be executed on a small number of SPs (32 on Fermi, 64 on Pascal).
How do they get a chance to execution?
The SM has 2 warp schedulers. What gets scheduled for execution on an SM are warps. So we must deal with 16 warps from 2 blocks.
Scheduling is done based on scoreboarding: each warp gets a score based on whether or not they have everything needed to execute (e.g. all operands, required SFU). The schedulers work at ½ the frequency of the SPs.

## Slide 125: [short/important topic]: Thread Index vs. Thread ID [critical in () understanding how SIMD is supported in CUDA, and () understanding the concept of “warp”]
Notes: Thread indices are a convenience to the programmer.
The actual threads are organized in a single, linear array of IDs.
This concept also very important in how threads are organized into warps.
Warps are important because the threads in a warp proceed in lock-step fashion (implications to thread divergence, etc.). Warps are the quantum unit of scheduling on an SM.
The index that runs faster is x, next y, slowest z.
For thread with thread index (4,2,3), the next one (for scheduling purposes) is thread with index (5,2,3)! Not (4,2,4)

## Slide 126: Organizing Threads into Warps
Thread IDs within a warp are consecutive and increasing
  Related to the 1D projection from thread index to thread ID
  Recall: in multidimensional blocks, the x thread index runs fastest, then y, then z
  Threads with IDs (0...31) combine into warp 0, threads (32…63) into warp 1, etc.
Partitioning of threads into warps is always the same
  You can use this in control flow
  Warp size has always been 32 and is unlikely to change soon
While you can rely on ordering among threads (each thread has a fixed ID, & the IDs are in sequence), DO NOT rely on any ordering among warps (there is no such thing)
  Warp scheduling is not under user control in CUDA
Notes: In other words, thread with ID 67 will always be in warp 2. You can use that!
(What you probably will use is that thread IDs 66 and 67 are in the same warp)
But you cannot count on, say, warp 1 to be always scheduled before warp 2!

## Slide 127: Threads are Organized & Executed as Warps
Each thread block split into one or more warps
If thread block size is not multiple of warp size, unused lanes go wasted
  Example: block w/ 50 threads – 64 lanes, of which last 14 lanes go wasted
The hardware schedules each warp independently
Warps within a thread block execute independently
Warp of 32 threads
Warp of 32 threads
Block of 128 threads
Warp of 32 threads
Warp of 32 threads
NVIDIA [J. Balfour]→
Notes: A block of 128 threads, color-coded in 4 colors (4 warps).
The warps are scheduled as a unit.
It is not required to have the block size a multiple of 32, but it’s a good idea!

## Slide 128: The nitty-gritty: hardware resources dictate what a capability can do
[NVIDIA]

## Slide 129: SM Warp Scheduling, more details
SM hardware implements almost zero-overhead warp scheduling
  A warp whose next instruction has its operands ready for use is eligible for execution
  Eligible warps are selected for execution on a prioritized scheduling policy
  All threads in a warp execute same* instruction
warp 9 instruction 11
SM multithreaded
Warp scheduler
warp 1 instruction 42
warp 3 instruction 35
warp 9 instruction 12
. . .
time
warp 3 instruction 36
Notes: Low overhead for changing context (unlike CPU)
This is because the context for each thread (e.g. registers) is already available (no need to pack/unpack this with the threads as done on the CPU).
Important to have many warps on an SM: better chance to find one that’s ready to be executed.
Note: on old cards (Tesla) there were only 8 SPs and one scheduler: 4 cycles needed for one instruction (for one warp). Fermi has 2 schedulers and 2x16 SPs that work at twice the frequency of the schedulers  1 instruction / cycle
This information is important because it can tell you how many warps are needed (for a particular code) to hide memory access latencies with useful computations. In this example: 34 warps minimum.
High arithmetic intensity  fewer warps needed to hide latencies.

## Slide 130: Fermi Specifics
There are two schedulers that can each issue one warp of “ready-to-go” threads
One warp issued at each clock cycle by each scheduler
During no cycle can more than 2 warps be dispatched for execution on the SM’s functional units
Scoreboarding used to figure out which warp is ready
Fermi SM
Notes: 4 function units:
16 ALU/FPU (integer/single precision)
16 ALU/FPU (integer/single precision)
4 SFU (for special mathematical functions)
16 LDST (load/store)
For double precision: both 1 and 2 are used
Scoreboarding looks at:
instructions being fetched/decoded
necessary resources (operands ready? SFU required?)
what instruction modifies what register
Two warps with same score are selected oldest-first

## Slide 131: Quick Remarks
GPU architecture is pipelined
  At each clock cycle one instruction can be retired
However, ILP support is relatively limited
  To the best of my knowledge:
    Fermi has no out-of-order execution smarts
    There is no prefetching
    There is no speculative execution
Note:
  The odd warp index are handled by a scheduler, the even ones are handled by the other scheduler
    No trading warps at run time between schedulers
    Pic makes this point too
even odd

## Slide 132: Fermi Specifics
As shown in picture, at no time can we see more than 2 warps being dispatched for execution during a cycle
Note that at any given time we might have more than two functional units working though (which is actually very good, device kept busy)
T i m e
Past
Present
Functional units
Notes: Because there are 2 schedulers: at most 2 instructions are dispatched for execution in a cycle.
But you can have more of them being executed at any given time! Indeed, an SFU for example needs 4 cycles to complete. Other warps that do not require them can be executing on other FUs (ALU, FPU, LDST)

## Slide 133: Good to know… When SM has multiple partitions (like Ampere)
A warp always runs on one of the four sub-partitions
  It does not change sub-partitions during execution
Each sub-partition holds up to 16 warps
  Per SM:
    4 partitions 16 warps
    64 warps max 2048 threads
[NVIDIA]

## Slide 134: Possible state of a warp (the interplay between warps & warp-scheduler)
  First possible state: Active Warps (deployed on an SM)
    A possible sub-state: Ineligible Warp (a subset of the Active Warps, waiting on data or functional units)
    Another possible sub-state: Eligible Warps (a subset of the Active Warps)
    Another possible sub-state: Issued Warps (formerly Eligible, now executing)
  Second possible state: Retired Warps (no more instructions left in the kernel for these Warps)
  Causes for a warp to be ineligible
    An instruction fetch
      Next instruction not available (super sad!!!)
    A memory dependency
      Result of memory instruction, e.g., load
    An execution dependency
      Result of previous instruction (recall data hazard in pipelining)
    A synchronization barrier (more on this later)
      E.g., __syncthreads()

## Slide 135: Execution Configuration, revisiting the concept
Prefer thread block sizes that result in mostly full warps
Bad: kernel<<<N, 1>>> ( ... )
Okay: kernel<<<(N+31) / 32, 32>>>( ... )
Better: kernel<<<(N+127) / 128, 128>>>( ... )
Many threads per block provide SM with many warps to switch between
  This is how the GPU hides memory access latency
Resource like amount of ShMem & size of RegFile may constrain number of threads per block
NVIDIA [J. Balfour]→
Notes: Do not launch N blocks each with 1 thread!
OK, but not great, to have 32 threads in 1 block (that’s only 1 warp)
Best: Use 128, 256 threads/block
But maximum number of threads in a block is limited by shared memory (for example – see later). That would limit the number of blocks resident on an SM. This may reduce occupancy.
The moral of the story: algorithms may need to be changed for parallel computing, maybe to something that would be ridiculous to do on a sequential architecture!
We will see this on matrix multiplication with shared memory

## Slide 136: Scheduling: Summing It Up…
When host invokes a kernel grid, the blocks of the grid are enumerated and distributed to SMs with available execution capacity
Number of resident blocks on one SM
  Up to 8 blocks (on Fermi)
  Up to 16 on Kepler & Turing
  Up to 32 on Maxwell, Pascal, Volta , Ampere
When a block of threads is executed on an SM, its threads are grouped in warps. The SM manages several warps at the same time
  Up to 48 warps can be managed by an SM on Fermi
  Up to 32 warps can be managed on Turing
  Up to 64 warps can be managed on Kepler, Maxwell, Pascal, Volta, Ampere
When a thread block finishes, a new block is launched on the vacated SM

## Slide 137
Thread Divergence
[pre-Volta]
Notes: New topic related to execution scheduling

## Slide 138: Thread Divergence in “if-then-else”
Handling of an if-then-else construct in CUDA
  First, a subset of threads of the warp execute one branch
    Execution moves forward for these threads in lockstep fashion
  Next, the rest of the threads in the warp execute the other branch
    Execution moves forward for these threads in lockstep fashion
After the if-then-else statement all threads of the warp move on in lockstep fashion
The system automatically handles control flow divergence, conditions in which threads within a warp execute different paths through a kernel
Often, this requires that the hardware execute multiple paths through a kernel for a warp
  For example, both the if clause and the corresponding else clause

## Slide 139: Thread divergence issues
__global__ void kv(int* x, int* y)
{
int i = threadIdx.x + blockDim.x * blockIdx.x;
int t;
bool b = f(x[i]);
if( b )
{ // g(x)
t = g(x[i]);
}
else
{ // h(x)
t = h(x[i]));
}
y[i] = t;
}
NVIDIA [J. Balfour]→
Notes: Some threads in the warp follow the if branch. The rest are idle.
Some threads in the warp follow the else branch. The rest are idle.

## Slide 140: Thread divergence issues
Nested branches are handled similarly
  Deeper nesting results in more threads being temporarily disabled
In general, one does not need to consider divergence when reasoning about the correctness of a program*
  Certain code constructs, such as those involving schemes in which threads within a warp spin-wait on a lock, can cause deadlock
In general, one does need to consider divergence when reasoning about the performance of a program
NVIDIA calls execution model SIMT (Single Instruction Multiple Threads) to differentiate from actual SIMD where threads really are in lockstep
NVIDIA [J. Balfour]→
Notes: You do not need to understand this to write code that runs correctly. The system handles this.
You need to worry about this for code that is performant.
Thread divergence is why NVIDIA calls their execution model SIMT. Subtle difference from SIMD: SIMT is SIMD for as long as the threads in a warp execute in lockstep mode; slightly different when threads diverge.

## Slide 141: Performance of Divergent Code
Performance decreases with degree of divergence in warps
Compiler and hardware can detect when all threads in a warp branch in the same direction
  Example: all take the if clause, or all take the else clause
  The hardware is optimized to handle these cases without loss of performance
    if (threadIdx.x / WARP_SIZE >= 2) { }
  Creates two different control paths for threads in a block
  Branch granularity is a whole multiple of warp size; all threads in any warp follow the same path. No warp divergence…
The compiler can also compile short conditional clauses to use predicates (bits that conditionally convert instructions into null ops)
  Avoids some branch divergence overheads and is more efficient
  Often acceptable performance with short conditional clauses
NVIDIA [J. Balfour]→
Notes: Note:
the presence of an if/else statement in a kernel function is not a problem by itself.
thread divergence concerns only divergence of threads within a warp!
Even for threads diverging inside a warp, in special situations (short sequences), the compiler can modify the code to remove thread divergence: all threads in a warp execute the same instructions, but some of those are replaced by the compiler with no-ops which do not write memory or registers.  acceptable penalty hit

## Slide 142: The “schedule optimizer” hardware asset
To maximize parallel efficiency, Volta includes a “schedule optimizer” which determines how to group together into SIMT units the active threads from the same warp
Threads can now diverge and re-converge at sub-warp granularity
While the scheduler supports independent execution of threads, it optimizes non-synchronizing code to maintain as much convergence as possible
  “convergence optimizer” still groups together threads that execute the same code to run them in parallel

## Slide 143: Handling thread divergence, Volta/Turing/Ampere
Instructions from the if and else branches can now be interleaved in time, as shown in the pic.
  NOTE: what’s shown in the pic is one possibility. How the scheduling takes place depends on the code being executed and be different than what shown in the pic
IMPORTANT: execution is still SIMT – at any given clock cycle, the same instruction is executed for all active threads in a warp just as before Volta
  NOTE: this is why the “schedule optimizer” tries to converge all threads
    If all converged, the 32 threads get to execute an instruction. Otherwise, only a subset of threads get to execute an instruction
Why bother with understanding this?
  Ability to independently schedule threads within a warp makes it possible to implement complex, fine-grained algorithms and data structures in a more natural way
[NVIDIA]

## Slide 144: Handling thread divergence, Volta/Turing/Ampere
Note that instruction Z is fairly likely not to be executed by all warp threads at the same time
Call CUDA warp synchronization function syncwarp() to force reconvergence (lower pic)
  The divergent portions of the warp might not execute Z together, but all execution pathways from threads within a warp will complete before any thread reaches the statement after the syncwarp()
Placing the call to syncwarp() before the execution of Z would force reconvergence before executing Z, potentially enabling greater SIMT efficiency if the developer knows that this is safe for their application
[NVIDIA]

## Slide 145: Example: Volta thread scheduling helps algorithm implementation
“Starvation-free algorithm” – a parallel algorithm that works on the presumption that a thread that participates in the implementation of the algorithm cannot be starved
NVIDIA GPUs prior to Volta: didn’t support starvation avoidance
  Indeed, one or more threads may repeatedly acquire and release a mutex while starving another thread from ever successfully acquiring the mutex
Example at right shows how Volta independent thread scheduling implements a starvation-free algorithm
  Inserting nodes into a doubly linked list in a multithreaded application
[NVIDIA]
Per-node locks are acquired (left) before inserting node B into the list (right).
Notes: Independent thread scheduling in Volta ensures that even if a thread T0 currently holds the lock for node A, another thread T1 in the same warp can successfully wait for the lock to become available without impeding the progress of thread T0. Note, however, that because active threads in a warp execute together, threads spinning on a lock may degrade the performance of the thread holding the lock.
It is also important to note that the use of a per-node lock in the above example is critical for performance on the GPU. Traditional doubly-linked list implementations may use a coarse- grained lock that provides exclusive access to the entire structure, rather than separately protecting individual nodes. This approach typically leads to poor performance in applications with many threads—Volta may have up to 163,840 concurrent threads—caused by extremely high contention for the lock. By using a fine-grained lock on each node, the average per-node contention in large lists will usually be low except under certain pathological node insertion patterns.

## Slide 146
The NVIDIA GPU Memory Ecosystem

## Slide 147: CUDA Memory Ecosystem, high vantage point [Note: picture assumes two blocks, each with two threads]
Image shows the memory hierarchy that a block sees while running on an SM
Each thread can:
  R/W per-thread registers
  R/W per-thread local memory
  R/W per-block shared memory
  R/W per-grid global memory
  Read only per-grid constant memory
  Read only per-grid texture memory
  Read only per-grid surface memory
Host can R/W global, constant, and texture* memory
  *: texture can be written only as “surface” mem
[UIUC]
(Device) Grid
Constant
Memory
Texture
Memory
Global
Memory
Block (0, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Host
One SM
Another SM
Notes: Global, constant, and texture memory spaces are persistent across kernels called by the same application.
“surface” memory is like “texture”, except that the former can be written (“texture” can only be read)

## Slide 148
IMPORTANT NOTE:
  Global, constant, and texture memory spaces are persistent between kernels called by the same host application

## Slide 149: What “register” means in CUDA
Any variable that you are using in a kernel at some point eats up a register
  The variable that you use – it needs to “live” somewhere
Then every single variable you use in a kernel will burn (at some point in the execution flow) a register
  NOTE: even a variable stored in ShMem, for it to be operated on, it’ll eat up a register* at some point in the execution
    *: except on Ampere, where one can actually control this…
As execution advances through a kernel, the number of registers occupied keeps changing
  What’s relevant: max number of registers required during the execution of the kernel
The complier controls/decides the register allocation when executing a kernel

## Slide 150: Programmer View of Register File
Number of 32 bit registers in one SM is as follows:
  8K registers in each SM in G80
  16K on Tesla
  32K on Fermi
  64K on Kepler and Maxwell, Pascal, Volta, and Ampere
Registers are dynamically partitioned across all Blocks assigned to the SM
Once assigned to a Block, these registers are NOT accessible by threads in other Blocks
A thread in a Block can only access registers assigned to itself
  IMPORTANT: A thread can have assigned by the compiler up to 255 registers
4 blocks
3 blocks
Possible per-block partitioning scenarios of the RF available on the SM

## Slide 151: Register related: a “level of parsimony” issue
Size of a register: 4 bytes
Is it that if you use a char in a kernel, then you don’t use a full register but rather ¼ of it?
Not really, unfortunately; i.e., there is no parsimony in usage of a register
  Any data type that requires less then or equal to 4 bytes eats up a register
    One char thus eats up an entire register
  If you use a double, it eats up two registers
Notes: See also https://devtalk.nvidia.com/default/topic/491309/int-vs-short-vs-char-in-kernels/

## Slide 152: The Concept of Local Memory [“local”: misnomer]
Physically, local memory does not exist
  In reality, data stored in “local memory” is placed in cache or the global memory at run time or by the compiler
What gets stored in local memory?
  Register spill, if too many registers are needed for computation (“high register pressure”)
  The stack of the thread
Quick observations:
  “Local” means that it’s got local scope; i.e., it’s specific to one thread and not visible to any other thread
  Local memory has the same latency as global memory, unless cached
(Device) Grid
Constant
Memory
Texture
Memory
Global
Memory
Block (0, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Host
Notes: Global, constant, and texture memory spaces are persistent across kernels called by the same application.

## Slide 153: Caches & the Shared Memory
Logically, there is a distinction between cache and shared memory
  That is, they are handled differently by the runtime
Physically, there is no difference between the two of them
  You can turn a “dial” and have more or less cache, that is, have less or more shared memory
Caches: controlled by the runtime
Shared memory: controlled by you (think of it as “fast scratchpad memory”)

## Slide 154: Caches & the Shared Memory
Fermi
  Each SM: 64 KB L1 cache & shared memory
  All SMs tap into a common 768 KB L2 cache memory
Pascal:
  Each SM: Unified 24 KB L1 cache
  Each SM: 64 KB shared memory
  All SMs tap into 4096 KB of L2 cache memory
Volta:
  L1 cache + Shared Mem = 128 KB per SM
  One can carve out of 128KB shared memory as follows:
    0 KB, 8 KB, 16 KB, 32 KB, 64 KB, or 96 KB
  What is not taken by the ShMem becomes L1 cache:
    128 KB, 120 KB, 112 KB, 96 KB, 64 KB, 32 KB
  All SMs tap into 6144 KB of L2 cache memory, visible to all SMs
IMPORTANT: Numbers reported are per SM
Fermi SM
Notes: The previous plot is bandwidth for moving data from/to global memory.
Each SM has local L1 cache (shared with shared memory, ratio under user control).
Fermi default: 48 KB shared / 16 KB L1 cache (can also do16/48)
Kepler: 48/16, 32/32, 16/48
Difference: shared memory is controlled by the user. L1 cache use is automatic. If you do not use shared memory, increase the chunk for L1 cache to allow the hardware to leverage it.

## Slide 155: Global, Constant, and Texture Memories
(Device) Grid
Constant
Memory
Texture
Memory
Global
Memory
Block (0, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Host
Global memory
  Main means of communicating R/W Data between host and device
  Contents visible to all threads
Texture and Constant Memories
  Constants initialized by host
  Contents visible to all threads
Global, texture and constant memories are accessible by host
  Done at high latency, low bandwidth
[NVIDIA]
NOTE: We will not emphasize texture in ME759.

## Slide 156: CUDA Device Memory Allocation/Deallocation
cudaMalloc()
  Allocates mem in the device Global Memory
  Requires two parameters
    Address of a pointer to the allocated object
    Size of allocated object
cudaFree()
  Frees mem from device Global Memory
    Requires a pointer to freed object
(Device) Grid
Constant
Memory
Texture
Memory
Global
Memory
Block (0, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Host

## Slide 157: CUDA Host-Device Data Transfer
cudaMemcpy()
  Memory data transfer
  Requires four parameters
    Pointer to source
    Pointer to destination
    Number of bytes copied
    Type of transfer
      Host to Host
      Host to Device
      Device to Host
      Device to Device
  Things happen over a PCIe connection
    Up to 16 GB/s (PCIe 3.0 x16, in each direction)
    Up to 32 GB/s (PCIe 4.0 x16, in each direction)
(Device) Grid
Constant
Memory
Texture
Memory
Global
Memory
Block (0, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Host
Notes: PCIe 4.0 16X (expected 2017)  almost 32 GB/s
NVLink (available on Pascal)  5-12 times faster than PCIe 3.0

## Slide 158: CUDA Host-Device Data Transfer (cont.)
Example:
  Transfer a number of “size” bytes
  M is in host memory and Md is in device memory
  cudaMemcpyHostToDevice and cudaMemcpyDeviceToHost are CUDA-defined constants
cudaMemcpy(Md.elements, M.elements, size, cudaMemcpyHostToDevice);
cudaMemcpy(M.elements, Md.elements, size, cudaMemcpyDeviceToHost);
Note: if you use gdb to debug, don’t expect to be able to read memory off a device pointer
  Debugging for GPU computing relies on cuda-gdb
Notes: Note: copy values in constant memory (from the host) using cudaMemcpyToSymbol
Example:
__device__ __constant__ pivalue;
float foo = 3.14159f;
cudaMemcpyToSymbol(&pivalue, &foo, sizeof(float));

## Slide 159: Memory Access Times
Register – dedicated HW on chip - single cycle NOTE: you don’t have control over this
Cache/Shared Memory – dedicated HW on chip – a few cycles NOTE: physically, like L1 cache
Local Memory – DRAM, (if not in cache - *slow*; if cached – relatively fast)
Global Memory – DRAM, no cache - *slow*; cached, is fast…
Constant Memory – DRAM, cached, 10s…100s of cycles, depending on cache locality
Texture Memory – DRAM, cached, 10s…100s of cycles, depending on cache locality
Instruction Memory (invisible) – DRAM, cached
Notes: Take away message: organize your code to use as much as possible the faster memory:
keep in mind the relative access times (some of these change with new hardware)
be careful how you organize data and what data you bring over (do not duplicate information)
Recall:
GPUs have much larger register files than a CPU
64K registers (each one word, i.e. 32 bits) per SM on Pascal
But you can also have up to 2048 threads resident per SM
So you end up with just 32 registers per thread!
In fact, NVIDIA sets an upper limit of 255 registers/thread

## Slide 160: Storage Locations
Memory | Location | Cached | Access | Who
Register | On-chip | N/A | Read/write | One thread only
Shared | On-chip | N/A | Read/write | All threads in a block
Global | Off-chip | Yes | Read/write | All threads + host
Constant | Off-chip | Yes | Read | All threads + host
Texture | Off-chip | Yes | Read | All threads + host
Off-chip means on the GPU but not on the SM, which translates into high latency.
Notes: Back in the day (Tesla C1060): global memory was not cached

## Slide 161: Putting things in perspective: The 3 most important GPU memory spaces
Register: per-thread basis
  Private per thread
  Can spill into local memory (potential performance hit unless cached)
Shared Memory: per-block basis
  Shared by threads of the same block
  Used for: intra-block inter-thread communication
Global Memory: per-application basis
  Available for use by all threads
  Used for: global access, all threads
  Also used for inter-grid communication
Thread
Register
Grid 0
. . .
Global
Memory
. . .
Grid 1
Sequential
Grids
in Time
Block
Shared
Memory

## Slide 162: Slightly from the left field
GPU virtual memory: 49-bit virtual address space mapped to physical memory located in 3 places
  On the device
  On the host, pinned system memory
  On a different GPU (peer memory)
Global memory is visible to all threads in the GPU
Global memory is accessed through the SM L1 and GPU L2
NVIDIA’s first take at fusing CPU& GPU (ARM architecture): white paper

## Slide 163: Example: Matrix Multiplication, Revisited
Purpose
  See an example where the use of multiple blocks of threads plays a central role
  Highlight the use/role of the shared memory
  Point out the __syncthreads() function call
NOTE: A one dimensional array stores the entries in the matrix
Notes: Here we will use a bus instead of a bunch of cars to bring over data from memory.
Savings come from the fact that bandwidth to accessing shared memory is ~10 better than global memory.
Thread synchronization becomes crucial to avoid race conditions

## Slide 164: A Critique of the Old Matrix Multiplication Example
One row of M is loaded N.width times
This happens for each row of M
Moral of the story: the matrix M is loaded N.width times
One column of N is loaded M.height times
This happens for each column of N
Moral of the story: the matrix N is loaded M.height times
Loading M and N over and over → not a good idea, memory transactions are expensive
Grid 1
Block 1
48
Thread
(2, 2)
width
M
P
N

## Slide 165: Why Revisit the Old Example?
In the naïve first implementation the ratio of arithmetic computation to memory transaction (“arithmetic intensity”) very low
  Each arithmetic computation required one fetch from global memory
  The entries in M are copied from global memory to the device N.width times
  The entries in N are copied from global memory to the device M.height times
No brownie points for moving data around
  Hundreds of cycles required for bringing data from global memory
  When solving a problem, the goal is to go through the machine instructions in your executable, not to wait for data to come your way
Notes: Data reuse is the goal

## Slide 166: Answering the question: “Could/Should I use Shared Memory?”
Figuring out whether you should use share mem
  Imagine you are a thread executing the code in the kernel
  If you, as a thread, use data that can also be used by another thread in your block, then you should consider using shared memory
Note: regardless of the above test, you can use shared memory as scratch pad memory
  Don’t let it go wasted, use for storing often-used variables even if they’re not used by multiple threads

## Slide 167: Rule of thumb
“try hard to organize your data structure and algorithms to make use of shared memory”
Organize data and use algorithms so that you can bring data in shared memory and subsequently use repeatedly by multiple threads in the block
  This is sounds like “locality”; the cache should help you to. Otherwise, take your destiny in your hands and use shared memory
    Your code is bound to run fast

## Slide 168: A Common CUDA Programming Pattern: Tiling w/ Shared Memory
Global memory access - much slower when compared to shared memory access
No brainer: Use shared memory, if possible
  Partition data into data subsets (tiles) that each fits into shared memory
  Handle each data subset (tile) with one thread block by:
    Loading the tile from global memory into shared memory, using multiple threads to exploit memory-level parallelism
    Performing the computation on the tile from shared memory; each thread can efficiently multi-pass over any data element of the tile
Notes: Recall: global memory: DRAM Shared memory: SRAM (split with L1 - Fermi or dedicated - Pascal)
Focus on data reuse
Introduce the concept of tiling (common programming pattern)

## Slide 169: Tiling used for Matrix-Matrix multiplication
One block computes one square sub-matrix Csub of size Block_Size
tx
A
B
C
Csub
Block_Size
wB
wA
Block_Size
Block_Size
ty
Block_Size
Block_Size
Block_Size
hA
wA
NOTE: A similar technique is used on CPUs to improve cache hits. See slide “Blocking Example” at
http://cseweb.ucsd.edu/classes/fa10/cse240a/pdf/08/CSE240A-MBT-L15-Cache.ppt.pdf
One thread computes one entry of Csub
Assumption: A and B are square matrices and their dimensions of are multiples of Block_Size
  Doesn’t have to be like this, but keeps example simpler and focused on the concepts of interest
  In this example work with Block_Size=16x16
Notes: We will have a first loop over tiles (moving left in A, moving down in B)
Then, inside a tile (i.e. a block), each thread will loop over a row in the A tile and a column in the B tile to calculate a piece of its final value (the red square in C)

## Slide 170: A Block of 16 X 16 Threads
Notes: We will have 256 (16x16) threads that will work in concert on a tile
They will bring together (in shared memory) one tile from A and one tile from B
Then, they each work separately on calculating an increment for their assigned C[i,j]
But they do so by sharing data!

## Slide 171
// Thread block size
#define BLOCK_SIZE 16
// Forward declaration of the device multiplication func.
__global__ void Muld(float*, float*, int, int, float*);
// Host multiplication function
// Compute C = A * B
// hA is the height of A
// wA is the width of A
// wB is the width of B
void Mul(const float* A,const float* B,int hA,int wA,int wB, float* C)
{
// Load A and B to the device
float* Ad;
int size = hA * wA * sizeof(float);
cudaMalloc((void**)&Ad, size);
cudaMemcpy(Ad, A, size, cudaMemcpyHostToDevice);
float* Bd;
size = wA * wB * sizeof(float);
cudaMalloc((void**)&Bd, size);
cudaMemcpy(Bd, B, size, cudaMemcpyHostToDevice);
// Allocate C on the device
float* Cd;
size = hA * wB * sizeof(float);
cudaMalloc((void**)&Cd, size);
// Compute the execution configuration *assuming*
// the matrix dimensions are multiples of BLOCK_SIZE
dim3 dimBlock(BLOCK_SIZE, BLOCK_SIZE);
dim3 dimGrid( wB/dimBlock.x , hA/dimBlock.y );
// Launch the device computation
Muld<<<dimGrid, dimBlock>>>(Ad,Bd,wA,wB,Cd);
// Read C from the device
cudaMemcpy(C, Cd, size, cudaMemcpyDeviceToHost);
// Free global memory
cudaFree(Ad);
cudaFree(Bd);
cudaFree(Cd);
}
Notes: Execution configuration:
blocks must all have 16x16 = 256 threads (take advantage of 2D layout)
how many blocks do we need? simple under our assumption that the matrix dimensions are multiples of the tile size
if not, more complicated (some tiles will “fall off” the matrix extent) this is messy and main part of frustration in CUDA computing

## Slide 172
Notes: bx = blockIdx.x the B (and C) matrix sub-block column index
by = blockIdx.y the A (and C) matrix sub-block row index
aBegin = wA * (by*BLOCK_SIZE) index of the first sub-matrix of A processed by the block
aEnd = aBegin + wA – 1
aStep = BLOCK_SIZE
bBegin = BLOCK_SIZE * bx;
bStep = BLOCK_SIZE * wB

## Slide 173
// Shared memory for the sub-matrices (tiles) of A and B
__shared__ float As[BLOCK_SIZE][BLOCK_SIZE];
__shared__ float Bs[BLOCK_SIZE][BLOCK_SIZE];
// Loop over all the sub-matrices (tiles) of A and B required to
// compute the block sub-matrix; moving in A left to right in
// a row, and in B from top to bottom in a column
for (int a = aBegin, b = bBegin;
a <= aEnd;
a += aStep, b += bStep) {
// Load tiles from global memory into shared memory; each
// thread loads one element of the two tiles from A & B
As[ty][tx] = A[a + wA * ty + tx];
Bs[ty][tx] = B[b + wB * ty + tx];
// Synchronize to make sure the matrices are loaded
__syncthreads();
// Each thread in this block computes one element
// of the block sub-matrix (tile). Thread with indexes
// ty and tx computes in this tile the entry [ty][tx].
for (int k = 0; k < BLOCK_SIZE; ++k)
Csub += As[ty][k] * Bs[k][tx];
// Synchronize to make sure that the preceding
// computation is done before loading two new
// sub-matrices of A and B in the next iteration
__syncthreads();
}
// Write the block sub-matrix to global memory;
// each thread writes one element
int c = wB * BLOCK_SIZE * by + BLOCK_SIZE * bx;
C[c + wB * ty + tx] = Csub;
}
// Device multiplication function called by Mul()
// Compute C = A * B
// wA is the width of A
// wB is the width of B
__global__ void Muld(float* A, float* B, int wA, int wB, float* C)
{
// Block index
int bx = blockIdx.x; //the B (and C) matrix sub-block column index
int by = blockIdx.y; //the A (and C) matrix sub-block row index
// Thread index
int tx = threadIdx.x; //the column index in the sub-block
int ty = threadIdx.y; //the row index in the sub-block
// Index of the first sub-matrix of A processed by the block
int aBegin = wA * BLOCK_SIZE * by;
// Index of the last sub-matrix of A processed by the block
int aEnd = aBegin + wA - 1;
// Step size used to iterate through the sub-matrices of A
int aStep = BLOCK_SIZE;
// Index of the first sub-matrix of B processed by the block
int bBegin = BLOCK_SIZE * bx;
// Step size used to iterate through the sub-matrices of B
int bStep = BLOCK_SIZE * wB;
// The element of the block sub-matrix that is computed
// by the thread
float Csub = 0;
Notes: if __shared__ does not appear: each thread sets aside 16x16 memory locations for As and 16x16 for Bs
that’s already double what could ever be in registers  spills to local memory
with __shared__ this memory is specific to the block and shared between all threads in the block!
attention: all threads bring over disjoint pieces of data
Why do we need the __syncthreads here? Only threads in the same warp proceed in lock-step fashion. But threads in different warps do not.
Who gets synchronized? Threads in the same block
Would it make sense to have a Cs in shared memory? No – recall the “test for using shared memory”; no other thread needs this information

## Slide 174: Synchronization Function
Synchronization accomplished through a device lightweight function
  void __syncthreads();
Synchronizes all threads in a block (acts as barrier for all block threads)
  Does not synchronize threads from two blocks
One more condition for execution to commence once all threads in a block reached the sync point:
  All global & shared mem. transactions made by these threads prior to __syncthreads() are visible to all block threads
  Used to avoid RAW/WAR/WAW hazards when accessing shared or global memory (more later)
Notes: Attention: do not put a __syncthreads in an if statement unless you can guarantee all threads in the block go through there!

## Slide 175: [warning] __syncthreads() & thread divergence
Be very cautious when using a __syncthreads() in a conditional
The actual behavior is not clear
  Some difference between the Programming Guide and what happens in reality
See here for discussion of how/when code deadlocks:
  https://stackoverflow.com/questions/6666382/can-i-use-syncthreads-after-having-dropped-threads
  https://stackoverflow.com/questions/15146886/conditional-syncthreads-deadlock-or-not
#include<cuda.h>
#include<iostream>
__global__ void badIdeaSynchronization(int* data)
{
int i = threadIdx.x + blockDim.x * blockIdx.x;
if ((i & 0x01) == 0)
{
data[i] = data[i] + i; // if not odd, come here
}
else
{
data[i] = data[i] + 2 * i; // come here if you're odd
__syncthreads();
}
}
int main()
{
const int numElems = 4;
int hostArray[numElems], *devArray;
//allocate memory on the device (GPU); zero out all entries in this device array
cudaMalloc((void**)&devArray, sizeof(int) * numElems);
cudaMemset(devArray, 0, numElems * sizeof(int));
//invoke GPU kernel, with one block that has four threads
hangs<<<1, numElems >>>(devArray);
//bring the result back from the GPU into the hostArray
cudaMemcpy(&hostArray, devArray, sizeof(int) * numElems, cudaMemcpyDeviceToHost);
//print out the result to confirm that things are looking good
std::cout << "Values stored in hostArray: " << std::endl;
for (int i = 0; i < numElems; i++)
std::cout << hostArray[i] << std::endl;
//release the memory allocated on the GPU
cudaFree(devArray);
return 0;
}